## Slide 1: Progress of HXMT Science Ground Segment: Calibration and Background analysis
Zhang Juan，on behalf of HXMT SGS Institute of High Energy Physics, CAS
9th IACHEC

## Slide 2: Outline
HXMT & Science Ground Segment(SGS)
SGS Calibration work and its current status
  --- Li Xiaobo, lixb@ihep.ac.cn
HXMT background analysis
Summary
May 10-15, 2014 IACHEC @ Warrenton

## Slide 3: 1. Introduction of HXMT & SGS
HXMT---
Hard X-ray Modulation Telescope
Orbit: ~550km,~43°
Collimated X-ray telescope
Payloads:
  HE(NaI/CsI, 20-250keV)
  ME(Si-Pin,5-30keV)
  LE(SCD,1-15keV)
  SEM(space environment monitor)

## Slide 4: Special design
Different FOV detectors: large, small, covered
Collimator co-axis, but FOVs fall into 3 groups according to their major axis direction
Useful in background analysis
LE
HE
ME
Theoretical psf of HE-15 small FOV detectors

## Slide 5
Visualization of HXMT detectors
SCD detectors of LE in one box:
Collimators of LE:
Collimators of ME:
Si-Pin detectors of ME in one box:

## Slide 6
HXMT SGS

## Slide 7: 2. Calibration data flows in HEASARC

## Slide 8: 2. Flow of HXMT-SGS Calibration
detSim
  Inputs:
    Mass model of instrument and environment
    Some commands to configure the simulation
  Outputs:
    Raw event files(ROOT files)
  External dependencies:
    GEANT4—toolkit for MC of particle interactions with matter from CERN
    ROOT– Data analysis package from CERN.
May 10-15, 2014 IACHEC @ Warrenton
detSim
Mass model
Comds.
Raw Evt. data
specSim
Cal. Params.
rsp
db
CALDB
rspGen
Data Analysis
software
Spectrum,
efficiency

## Slide 9
specSim
  Inputs:
    Raw event root files
    Calibration parameters from experiment data
  Outputs:
    Energy response curve and efficiency
    FITS file, like rmf, arf.
  External dependencies:
    ROOT– Data analysis package from CERN.
    CCFITS—FITS data file I/O
rspGen
  Inputs:
    FITS file from CALDB
    Some FTOOLS to generate the RMF of observe ID.
  Outputs:
    Application RMF files
  External dependencies:
    CCFITS—FITS data file I/O
    FTOOLS of CALDB related.
Continue:
Incident Generator
Geant4
Mass Model,
Physical interaction model
Hit information
Deposit energy
Deposit position
Digitization
ADC spectrum,
Pulse width spectrum
Energy resolution and scale
All kinds of incident particles

## Slide 10: Current Status---HE
Detector :thinkness*diameter
Be-window：1.5mm*212mm
NaI：3.5mm*190mm
CsI：40mm*190mm
Rad Src. | E(keV) | chn | deltaE/E | Det eff.
Am241 | 59.5 | 50.1 | 15.5% | 100%
Co57 | 122.1 | 99.7 | 12.2% | 70%
Ba133 | 33.0 | 26.4 | 21.0% | 100%
 | 81.0 | 68.4 | 12.9% | 97%

## Slide 11: Current Status---HE
HE: Energy scale and resolution  rsp
241Am@ HE
C=2.515*E+1.614
σ/E=0.006+0.47/sqrt(E)
The difference between MC spectrum and data decides the precision of the energy response.
Experience to tune the MC parameters to reduce the difference .
Rad Src. | E(keV) | chn | deltaE/E | Det eff.
Am241 | 59.5 | 50.1 | 15.5% | 100%
Co57 | 122.1 | 99.7 | 12.2% | 70%
Ba133 | 33.0 | 26.4 | 21.0% | 100%
 | 81.0 | 68.4 | 12.9% | 97%

## Slide 12: Current Status---ME (Si-PIN)
ME: Energy scale and resolution@Panter
ME: efficiency, MC vs exp. ：
E>4keV &&E<30keV

## Slide 13
Current Status--- LE(SCD)
Efficiency @MC
Si-K：1.839keV
4 ×
100*100 pixels
L-shape readout mechanism

## Slide 14: LE: energy scale and resolution@Panter

## Slide 15: LE Simulation
only considering energy scale + resolution
Energy scale + resolution+
diffusion , drift and collection effects of charges
production of rsp is on-going

## Slide 16: 3. HXMT background simulation
Background rate
  Take HE as an example, in the day of 100 after launch
  CXB~48.0
  CR-p：62.7 prompt
  CR-p：116.3 delayed
  SAA：339.2
  Albedo gamma：75.5
  HE total bg rate~650cnt/s
  RXTE/HEXTE~80-110cnt/s@each cluster(800cm2)
   HE(5000cm2) 500-680cnt/s
SAA induced bg decrease with time after per passage of SAA
SAA-induced bg increase with days after launch due to the activation of long –lived nuclides

## Slide 17: 3. in-orbit BG subtraction method
Combined FOV method
Covered detector: Cc=nc*t*fp
Small detector: C­s=ns*t*(fs*A+fCXB*FOVs+fp)
Large detector: C­L=nL*t*(fs*A+fCXB*FOVL+fp)
off-axis method
FOV direction-1: C­1s=n1s*t*(fs*A*a1s+fCXB*FOVs+fp)
FOV direction-2: C­2s=n2s*t*(fs*A*a2s+fCXB*FOVs+fp)
FOV direction-3: C­3s=n3s*t*(fs*A*a3s+fCXB*FOVs+fp)
Principle
L
L
These two methods are based on the condition that:
Aperture background is proportional to FOV size,
Non-aperture background is identical for each detector.

## Slide 18: Preliminary bg simulation results
Aperture background of cxb:
  Covered det. ~ 0
  Large/small ~ 5
Non-FOV bg ratio of cxb:
  large/covered ~ 1.44
  Inner circle small/covered ~ 1.12
  Outer circle small/covered ~ 1.02
Using in-orbit obs. data to determine these parameter, background analysis method and the uncertainties

## Slide 19: 4. Summary
Now we focus on the construction of caldb, based on MC simulation and ground exp. data
  More experimental data are needed
Background: using MC data analysis the subtraction method
  In-orbit backgournd subtraction would be more complicated
Thank you for you attention