## Slide 1: Status of the Astrosat mission
A R Rao
Tata Institute of Fundamental Research, India

## Slide 2: Plan
Astrosat
Astrosat Instruments:
- Ultraviolet Imaging Telescope (UVIT)
- Large Area Xenon Proportional Counters
(LAXPC)
- Soft X-ray Telescope (SXT)
- Cadmium Zinc Telluride Imager (CZTI)
- Scanning Sky Monitor (SSM)
Calibration
- CZT – Imager
Conclusions

## Slide 3
LAXPC
UVIT
SXT
CZTI
SSM
Star Sensors
ASTROSAT

## Slide 4: Participating Institutes…
ISRO Centers
Satellite, rocket, T&E, Launch, Orbit, SSM,
Level 1&2 software + overall management
Research Institutes
Tata Institute of Fundamental Research
LAXPC, CZTI, SXT
Indian Institute of Astrophysics UVIT
IUCAA SSM, CZTI
RRI LAXPC
PRL, Universities,
Leicester Uty (SXT), Canadian Space Agency (UVIT)

## Slide 5
ASTROSAT
IRS (Indian Remote Sensing) Class
Launch PSLV from SHAR
Altitude : 650 km; Inclination : 6 deg.
Mass 1550 kg. (780 kg. Payloads)
Power : 2200 watts
200 Gb (210 Mb/sec)
Satellite Positioning System for orbit and time data
Payload pointing (3 ): 0.05 degree
Slew rate : 0.6 deg/sec
Launch: Second quarter of 2015
Operational life > 5 years
Slide courtesy: K S Sarma

## Slide 6: UVIT: Two Telescopes, Three Bands
f/12 RC Optics
Focal Length: 4756mm; Diameter: 38 cm
Simultaneous Wide Angle ( ~ 28’) images in FUV (130-180 nm) in one and NUV (180-300 nm) & VIS (320-530 nm) in the other
MCP based intensified CMOS detectors
Spatial Resolution : 1.8”
Sensitivity in FUV: mag. 20 in 1000 s
Temporal Resolution ~ 30 ms, full frame ( < 5 ms, small window )
Gratings for Slit-less spectroscopy in FUV & NUV (R ~ 100)
Getting ready for satellite integration (next 2 months).

## Slide 7: Soft X-ray Telescope (SXT)
Telescope Length: 2465 mm (Telescope + camera + baffle + door)
Focal Length: 2000 mm
Epoxy Replicated Gold Mirrors on Al substrates in conical Approximation to Wolter I geometry.
Radii of mirrors: 65 - 130 mm; Reflector Length: 100 mm
No. of nested shells : 40
No. of reflectors: 320 (40 per quadrant)
Detector : E2V CCD-22 (Frame-Store) 600 x 600
Field of view : 41.3 x 41.3 arcmin PSF: ~ 2 arcmins
Sensitivity (expected): 15 Crab (0.5 cps/mCrab)
Slide courtesy: K P Singh
Calibrated and Integrated with satellite
(next talk: A. Read)

## Slide 8
Three identical xenon filled proportional counters. Multi layer and multi cell geometry with 60 anode cells and 28 anti cells
Xenon + methane mixture at a pressure 1500 mm of Hg.
50 micron thick aluminized Mylar window with a FOV of 1ox1o
LAXPC:
Large area Xenon-filled
Proportional Counters
Energy range : 3 – 80 keV
Time Resolution: 10 sec
Area : 6000 cm2
(7980)
E /E ~ 3 - 7
Slide courtesy: Ravi Manchanda
One Unit calibrated and delivered for satellite integration.

## Slide 9: CZT-Imager
Side joining plates
Collimator
CZT top hsg.
CZT bottom hsg.
Radiator
Heat pipes
Optical cube
Alpha tag source
Handling brackets
CFRP support
CAM
Size: 482 x 458 x 603 mm
Weight - 50 kg
Collimator: 6 x 6 Degree
17 x 17 Degree
Power – 60 Watts

## Slide 10
Area | 1024 cm 2
Pixels | 16384
Pixel size | 2.4 mm X 2.4 mm (5 mm thick)
Read-out | ASIC based (128 chips of 128 channels)
Imaging method | Coded Aperture Mask (CAM)
Field of View | 17 X 17 deg2 (uncollimated) 6 X 6 (10 – 100 keV) – CAM
Angular resolution | 8 arcmin
Energy resolution | 5% @ 100 keV
Energy range | 10 – 100 keV - Up to 1 MeV (Photometric)
Sensitivity | 0.5 mCrab (5 sigma; 104 s)
Calibrated; final testing going on (Satellite Integration in next 2 months)

## Slide 11
3 PSPC; Area 60 cm2 (5 keV); Ang res. : 2.5o & 12’
Energy Res 20%@ 6 keV
Flight Models are being tested
(Satellite Integration in next 2 months)
Scanning Sky Monitor (SSM)

## Slide 12
Slide courtesy: S S Sarma
Payload integration, alignment & testing: December 2014; Launch: mid-2015

## Slide 13
Astrosat: Special Features
Low Inclination
Continuous time-tagged individual photon data
(LAXPC & CZTI)
– a few tens of micro-second accuracy
Bright source observing capability of SXT
Facility to change/ adjust observation time of
SSM pointing.
Hard X-ray (above ~ 80 keV) monitoring capability.

## Slide 14: Astrosat calibration: ground & onboard
Slide courtesy: G C Dewangan

## Slide 15
Slide courtesy: K P Singh
CCD: Optical illumination
CCD: X-ray illumination
Mn Kα, Kβ
145 eV resn.

## Slide 16: LAXPC Calibration
Radio-active sources for
Spectral Calibration.
GEANT4 simulation for background estimation

## Slide 17: CZT Calibration
4 Quadrants
64 Detectors
16,000 pixels
Multi-temperature, multi-sources

## Slide 18: Physics based model and fraction of counts in tail
Mu-Tau based method:
Photo-peak Efficiency
59.54 keV 81 keV 122 keV
99% 87% 84%

## Slide 19: CAM calibration: 2m length
A few arc-seconds could be achieved.

## Slide 20
The time difference (Delta T) in units of micro-seconds, is well within the expected calibration for pulse from a normal (1 ppm) clock.

## Slide 21: Polarization
 | Next (%) | 1:2 | 3:4 | 4:5
Obs | 2.4+0.1 | 4.3+0.2 | 0.8+0.1 | 8.0+2.0
Monte Carlo | 2.43 | 4.9 | 1.0 | 10.0
Crab 3 sigma detection in < 1 day

## Slide 22
Modulation Curve at 0 degree
10.78 % edge modulation fator
4.8 % corner modulation factor
Modulation Curve at 90 degree
-7.802 % edge modulation fator
2.57 % corner modulation factor

## Slide 23
Polarization measurement capability of CZTI
Arrows represent incident polarization direction
Slide courtesy: Santosh Vadawale

## Slide 24: Onboard Calibration
Low Energy: standard sources
High energy: Crab

## Slide 25: ASTROSAT: Observation Phases and Data Policy
Slide courtesy: K S Sarma

## Slide 26: Science Working Group and Payload Science Teams
PI: S Seetha (seetha@isro.gov.in)
UVIT: S. Tandon (sntandon@iucaa.ernet.in)
LAXPC: J. S. Yadav (jsyadav@tifr.res.in)
SXT: K.P. Singh (singh@tifr.res.in)
CZTI: A. R. Rao (arrao@tifr.res.in)
SSM: M. C. Ramadevi (ramadevi@isac.gov.in)

## Slide 27: `Hard X-ray Astronomy: Astrosat and Beyond’
A conference in Goa: September 24 - 26, 2014

## Slide 28: Conclusions
Wide band X-ray spectroscopy is the strength of Astrosat.
Extensive ground calibrations completed. Results are as expected.
New features (individual photon counting and possibly polarization) will enhance the observation capabilities.
Onboard calibration will center around Crab observation for high energy instruments.