## Slide 1: Charge transport model for Swept Charge Devices (SCD)
P. S. Athiray
Post Doctoral Research Fellow,
Manipal Centre for Natural Sciences,
Manipal University, Manipal
Collaborators : C1XS & CLASS team (ISRO Satellite Centre),
Dr. Jason Gow (The Open University, UK)
Dr. Sreekumar (Indian Institute of Astrophysics, Bangalore)

## Slide 2: C1XS achievement - First detection of Na
The best fit to one of the C1XS spectrum with all components
6th July 2009 (17:10:47 -17:13:59)
1.04 keV
  First direct measurement of enhanced Na abundances from the lunar surface

## Slide 3: Swept Charge Device (SCD) (Developed by e2V technologies Ltd., UK)
1D X-ray CCD
Continuous diagonal clocking
  Minimize surface generated
  leakage current
  High rate of periodic charge
  clocking (100 kHz/sample)
High spectral performance
with minimal cooling
CCD-54 used in C1XS

## Slide 4: SCD (CCD-54) in C1XS
Depletion depth ~ 35 – 40 µm
On-board resolution ~ 153 eV @ 6keV with -10o C
Heritage
  SMART-1 (DCIXS)
  Chandrayaan-1 (C1XS)
Pitch - 25µm
Each unit area – 1.07 cm2
Measured X-ray charge
CCD-54 used in C1XS
Notes: The SWD was developed by e2v technologies as an industrial X-ray spectrometer for the energy range of 0.5 keV to 10 keV, achieving near fano limited spectroscopy at -10oC.
The device has a three phase electrode structure, as depicted by the dashed lines (click mouse) the charge deposited by an X-ray event is clocked towards the central transport channel and towards the output amplifier to produce a linear output consisting of 575 pixel, unlike a conventional CCD it can not be used as an imager. There are two separate central channels for each side of the device which join just before the output.
The key technology of the SCD is the use of continuous clocking, similar to dither mode clocking and is used to minimise the surface generated leakage current. Through avoidance of an image integration period, the high rate periodic charge clocking (approximately 100 kHz/sample) produces a suppression of the surface leakage current due to maintaining the silicon surface inversion. The SCD is capable of providing similar performance at -20oC to a Si(Li) detector operating at -120oC.

## Slide 5
Better understand Spectral Redistribution Function (SRF) - RMF
  Reduce uncertainties in spectral response
Augment calibration
Improved global lunar elemental mapping using Chandrayaan-2 Large Area Soft x-ray Spectrometer (CLASS)
Motivation for Charge Transport Model

## Slide 6: Spectral Redistribution Function (SRF) of SCD
Photopeak
LE rise
LE tail
Escape peak
Cutoff
LE
shoulder
Observed SRF of SCD CCD54 at 8 keV – C1XS calibration
Narendranath et al., 2010
Complex SRF
Physical model for photon interaction and charge propagation

## Slide 7: Charge Transport Model (CTM) for SCD
Generic photon source input
  Photons spectrum on top of CCD
  Spatial distribution : Uniform source, Different geometry
Photon interaction, charge-cloud spreading, escape peaks, pixel mapping and charge collection
Simulate diagonal clocking and readout - output
  Raw pseudo linear output, Event selection with thresholds

## Slide 8: CTM for SCD
Monte Carlo simulation
Ideal Si based X-ray detector
Written in IDL with the aim to be generic
Interactions considered
  Field zone, Field free zone, Channel stop
Photon loss
  Dead layer & substrate

## Slide 9
V
Buried Channel
35µm
15µm
600µm
~1.5µm
Dead layer
(recombine)
Field zone
(drift)
Field-free zone
(diffusion)
Substrate
(recombine)
Interaction zones
&
Dominant physics
Drawn not to scale

## Slide 10: Equations governing CTM of SCD
Assumes Charge cloud distribution
is Gaussian – Pavlov & Nousek 1999
Kurniawan & Ong 2007
Hopkinson 1984;
Pavlov & Nousek 1999

## Slide 11: Equations governing CTM of SCD
Channel stop
  Followed steps similar to ACIS modeling
  Currently assumed energy independence for tuning parameters (α and χ)
Townsley et al., 2002

## Slide 12: Event selection in C1XS
Single Pixel event

## Slide 13: Spectral components of SCD
Interaction zone | SRF components
Channel stop | LE shoulder, LE tail
Field-free zone | LE rise, LE tail
Field zone | Photopeak, LE shoulder, LE tail, cutoff, Escape peak
8.047 keV
4.510 keV

## Slide 14: CTM results Vs C1XS ground calibration
5.414 keV
8.047 keV

## Slide 15: Energy dependence of SRF
Systematic variations
Channel stop interactions?
Concentration of dopants in the boundary?
Possible suggestions for further improvements!

## Slide 16: Summary of CTM
Modeled photon interaction, charge generation & propagation in SCD
Identified major sources contributing to the observed SRF
  CTM results matches well with C1XS ground calibration data
Studied Energy dependence of SRF
  Fraction of off-peak events are underestimated in CTM
  Fine tuning of channel stop interactions required

## Slide 17: SCD (CCD 236) for CLASS
Each unit – 4 cm2
2phase clock
Pitch – 100 µm
  Less split fraction
CLASS – 64cm2

## Slide 18
CCD-236 being used in CLASS
Measured X-ray charge

## Slide 19: Data comparison
Courtesy - Dr. Jason, Dr. Phillipa, The Open University, UK

## Slide 20: Future Work
Detailed study of dead layer interaction
  Investigate dead layer interactions (Si – SiO2 – Si3N4)
Investigation of Channel stop interactions
  Energy dependence and SRF contribution
Testing and validation for Bulk SCDs
Optimizing event selection and split threshold

## Slide 21: Thank You

## Slide 22
35µm
15µm
600µm
~1.5µm
Dead layer
(recombine)
Field zone
(drift)
Field-free zone
(diffusion)
Substrate
(recombine)
V
Buried Channel
Interaction zones
&
Dominant physics

## Slide 23
Field zone
Substrate
FF zone
Single pixel
events
Drawn not to scale – CCD 54

## Slide 24
Substrate
Multi pixel
events
Drawn not to scale – CCD 54
FF zone
Field zone

## Slide 25: Equations governing CTM of SCD

## Slide 26: Remote sensing X-ray studies of the Moon
Apollo 15,16 (XRS); SMART-1 (DCIXS); KAGUYA (XRS)
CHANDRAYAAN-1 (C1XS)
  First lunar bound XRF experiment to observe the Moon with a good spectral resolution

## Slide 27: CTM for SCD
Written in IDL with the aim to be generic
Implementation of the SCD architecture
  Diagonal charge transfer
  Pseudo linear charge output
Event processing in SCD (adopted in C1XS)
  Selection and optimization of event selection criteria
  Optimize event and split threshold
Study the SRF and its dependencies

## Slide 28: Motivation for Charge Transport Model
For accurate lunar surface composition
  High sensitive and resolved measurement of major rock-forming elements (Na, Mg, Al, Si, Ca, Ti, Fe)
  Reduce uncertainties in the derived XRF line fluxes
To better understand Spectral Redistribution Function
  To reduce uncertainties in spectral response
  Dependencies : Energy, Event selection criteria
Improved global lunar elemental mapping using
Chandrayaan-2 Large Area Soft x-ray Spectrometer (CLASS)

## Slide 29: Spectral Redistribution Function (SRF) of SCD
Energy
counts
Detector
Photopeak
LE rise
LE tail
Escape peak
Cutoff
LE
shoulder
Observed SRF of SCD CCD54 at 8 keV – C1XS calibration
Physical model for photon interaction and charge transportation to understand the complex SRF of SCD
E
Narendranath et al., 2010

## Slide 30: Outline of the talk
Chandrayaan-1 X-ray Spectrometer – An overview
Introduction to Swept Charge Devices
Need for a charge transport model
  Algorithm development and implementation
  Validation with ground calibration data
Application of model for the upcoming Chandrayaan-2 X-ray spectrometer (CLASS)