## Slide 1: Charged Particle Monitor onboard the ASTROSAT
Yash Bhargava
Tata Institute of Fundamental Research
On Behalf of CZTI/CPM team
1st March 2016

## Slide 2: Motivation for CPM
South Atlantic Anomaly
  Drifting
  Solar flares
Effect of Charged particles on the detector
Notes: Brief description of the SAA,
Effect of SAA on detector
Explain the czti plot

## Slide 3: CPM design
Scintillating crystal detector – CsI(Tl)
Light detector – Photodiode with CSPA
  Cost Effective
  No gain change
Notes: Contents of the circuit
Detector, Photodiode with pre amp
Processing electronics
Interface with the ground

## Slide 4: CPM logic
Notes: Explain the logic of the CPM
Incident proton produces radiation
Radiation converted to the electrical signal with the diode and amplified by the cspa
The signal reaches comparator, (mention the programmable part of LLD)
Free running counter to count the signals
Concept of gating time
Count preset values to discriminate SAA
False trigger avoidance
SAA signal generation

## Slide 5: Ground Calibration

## Slide 6: Spectral Fitting
Absence of direct energy information
Multi-Channel Analyser – used in engineering model
Integral spectrum using LLD
Gaussian fitting to determine the peak position
Notes: Mention where mca can be used for the energy information
Explain the spectrum generation process from LLD
Mention the use of peak position

## Slide 7: Testing with different sources
Radioactive sources – Ba133, Cs137 and Eu152
Detector response 1.20 mV/keV
Source | Energy (in MeV) | Peak Channel number
Ba133 | 356 | 43.1
Cs137 | 662 | 85.2
Eu152 | 1112 | 131
Eu152 | 1408 | 173.6
Chart: Photon Energy (in keV)
| 356 | 662 | 1112 | 1408
Peak | 43.1 | 85.2 | 131 | 173.6
Notes: Mention why testing with gamma sources is done

## Slide 8: Testing with particles
Tested in BARC-TIFR Pelletron facility
Protons of energy 15 MeV, 17 MeV and 18 MeV used
Attenuation observed due to air column, Teflon, Aluminum Mylar
Energy (MeV) | Peak channel number | Error in energy(MeV)
6.07 | 177.5 | 0.7
10.1 | 378 | 0.45
11.7 | 448.7 | 0.35
Chart: Proton Energy (in MeV)
| 6.07 | 10.1 | 11.7
Peak channel number | 177.5 | 378 | 448.7
Notes: Mention how the attenuated energy was computed
Mention that the fitting was done using the attenuated energy

## Slide 9: Stability tests
Detector exposed to the source for varying time durations
Stability in Peak position and PWHM is observed
Chart: Stability with time
| 10 | 100 | 500 | 1000 | 5000 | 10000 | 20000
October 25, 2010 | 170 | 168 | 171 | 169 | 168 | 168 | 167
November 30, 2010 | 184.15 | 187.52 | 186.93 | 185.66 | 187.01 | 186.63 | 187.69
Notes: Variation in peak- think of what can cause such variation
Mention the reason for the difference in the mean values

## Slide 10: Stability with environment
Detector tested in Thermo-Vacuum chamber
-10oC to 40oC
Stable results in 10-30oC
Notes: Mention that commercial grade detector was used. Best performance in RT range

## Slide 11: Onboard testing

## Slide 12: Switching ON
Default values
  Gating time 5 s
  Count threshold 3 counts/s
  Entry trigger criteria - 3
Notes: Effect of precession
Deepest SAA counts
Detection of SAA in grazing orbits

## Slide 13: Contour of SAA
Notes: Plotting the path of satellite
Plotting the contour maps for defining the boundaries well

## Slide 14: Onboard Stability of CPM
Mean and Variance of observed counts binned by square degree interval
Clear segregation between SAA and non SAA regions
Notes: Mean of counts vs the std
Low counts in non-SAA region – low variance means high stability of non SAA
Clumping of the non SAA region
Tracks of SAA region
- High variability within the degree

## Slide 15: Products from CPM
Monthly contour maps of SAA
Average counts in each square degree of Satellite path for ready reference
SAA window for Astrosat (in case CPM trigger fails)
  Currently set at 100oW to 0oE for all possible latitudes
  Trapezoidal window can be set for more data time
Notes: Contour maps can be used for model generation

## Slide 16: Thank you!