## Slide 1
NICER Calibration: Ground-based Results and In-Flight Plans
Craig Markwardt & Bev LaMarr
GSFC

## Slide 2: NICER: Astrophysics Mission of Opportunity on the International Space Station
PI: Keith Gendreau, NASA GSFC
Science: Understanding ultra-dense matter via soft X-ray timing spectroscopy of neutron stars
Platform: International Space Station ExPRESS Logistics Carrier external attached payload, with active pointing
Launch: NET January 2017, SpaceX-11 resupply
Duration: ≥ 24 months
Instrument: X-ray (0.2–12 keV) “concentrator” optics and silicon-drift detectors; GPS position & absolute time tagging
Enhancements:
  Demonstration of pulsar-based navigation
  Guest Observer program in Year 2+
Status:
  Ground-based calibration complete Fall 2015
  Passed PER, Winter 2015

## Slide 3: Unique Capabilities, New Discovery Space
Spectral band: 0.2–12 keV
  Well matched to neutron star emissions
  Overlaps RXTE, XMM-Newton, and other missions
Energy resolution: < 150 eV @ 6 keV
  10x better than RXTE
Timing resolution: 100 nsec RMS absolute
  50x better than RXTE
  > 100x better than XMM-Newton
Non-imaging FOV: 6 arcmin diameter
  10x finer than RXTE
Sensitivity: 5.3 x 10–14 erg/s/cm2 (5σ, Crab- like spectrum, 0.5–10 keV in 10 ksec)
  20x better than RXTE
  3x better than XMM-Newton’s timing capability (PN clocked mode)
An unprecedented combination of sensitivity, timing, and energy resolution

## Slide 4: NICER Calibration and Data Pipeline
Status of Ground Calibration as of Pre-Environmental Review
In-Flight Calibration

## Slide 5: Objectives of XTI Calibration
Develop instrument model to properly interpret science data
Calibrate instrument model with key measurements of flight and ETU hardware
Gain experience with extended operation (search for rare behaviors)
In-Flight calibration plan to verify calibration and/or adjust for post-launch shifts, cross-calibrate with other X-ray missions
Team Members
  System: C. Markwardt, K. Gendreau, Z. Arzoumanian
  XRC: T. Okajima, E. Balsamo, T. Enoto, L. Jalota
  FPM: R. Remillard, B. Lamarr, G. Prigozhin, D. Malonis
  Timing: L. Winternitz, J. Mitchell, E. Rogstad

## Slide 6: XTI Calibration Requirements
Component | Knowledge Requirement
Effective Area (Total @ 1-2 keV) | 10%
Energy Gain | 1%
Resolution (FWHM) | 10%
Background | 10%
Timing Uncertainty (Total, 1s) | 100 ns

## Slide 7: XTI Calibration & Alignment Flow
56 FPMs & Spares
2 Reference FPMs
Relative Calibration @ MIT
  MXS Fluorescent Lines C-K, F-K, Al-K, Ti-K, Cu K
  Additional tests for selected sample
56 XRCs & Spares
Effective Area & PSF Measurement @ GSFC Beamline
Selected sample: off-axis measurement
“Absolute” Calibration @ BESSY
XRC Integration into XTI Optical Bench @ GSFC
Alignment in 1 m parallel optical beam, flux maximization
Relative alignment of XRC flats
FPM Integration @ GSFC
Translation adjustment in 1 m parallel beam, flux maximization
Payload I&T Winter 2015/2016
Detector Response Model
Optics Response Model
XTI
Sep 2014- June 2015
July-Nov
2014
Offline
Fall 2015
July-October 2015

## Slide 8: Optic and Detector Efficiency
X-rays
Thermal Film
MODEL: transmission model (thickness) MEASUREMENT: BESSY transmission on window samples ACHIEVED: <1% relative transmission ✔︎
X-ray Concentrator
MODEL: X-ray ray tracing (mirror area)
AREA MEASUREMENT: X-ray beam, each optic ACHIEVED: <4% uncertainty, >20% margin ✔︎ PSF MEASUREMENT: X-ray beam, each optic ACHIEVED: <4% uncertainty, >4% margin ✔︎ COALIGNMENENT MEASUREMENT: optical vignetting, each optic ACHIEVED: ~25” uncertainty ✔︎
Detector Window
MODEL: X-ray transmission model (thickness)
MEASUREMENT: BESSY transmission on window samples ACHIEVED: < 1% relative transmission ✔︎
FPM Silicon Drift Detector
MODEL: Silicon / X-ray (Scholze & Procop 2009) GAIN & RESOLUTION MEASUREMENT: X-ray lines, each FPM and MPU ACHIEVED: <1% gain uncertainty ✔︎ and meet resolution ✔︎
RESOLUTION MEASUREMENT: relative area, gain, resolution with MXS & fluorescent line source

## Slide 9: Energy Resolution of All 56 Detectors Over Wide Temperature Range During XTI TVAC
Gain and Resolution Requirements Met ✔︎

## Slide 10: Energy Resolution Requirement Met
Red points: TVAC data with Fe55 source, all detectors and all temperatures combined (Cycle 3, T = –5 ºC to +70 ºC)
Blue points: FPM calibration data with multi-line modulated X-ray source @ MIT, all detectors combined, single temperature (T ~ 30 ºC)
Red & blue curves: Fits to Fano-limited readout noise performance curves demonstrate that XTI’s spectral resolution meets both the original and relaxed requirements.
Current requirement
Requirements Met ✔︎

## Slide 11: BESSY Detector Filter Transmission Data
In September 2015, MIT brought all the reference SDDs used in calibration of the flight detectors to the BESSY synchrotron for absolute calibration.
In addition to the SDDs, MIT brought some detector windows and XRC thermal shields.
To the right is transmission data from one of the detector windows showing that it meets requirements.
On MIS, this data is at:
Doc #: EXP-NICER-FPMMPU-REF-0225
Title: MIT Filter KW37
Detector Spec (DS-023) requires detector efficiency >67% at 1.5 keV. This is dominated by the detector window, where we see a transmission of 89.73% ✔︎
DS-027 requires the detector window has transmission of >79% ✔︎
DET-08 requires >55% at 392 eV, >65% at 677 eV, and >=80% at all energies above 4.5 keV.
This data verifies all this ✔︎
Margin

## Slide 12: Module Co-Alignment
Module co-alignment was measured using optical vignetting scans
Final measurements (right) establish baseline co-alignment knowledge vector for each module
Uncertainty 20.2” ~25”requirement met ✔

## Slide 13: System Level Time Resolution Calibration Measurement
1s = 85.5 ns
100 ns Requirement Met ✔︎
Notes: ----- Meeting Notes (11/30/15 09:38) -----
use Lukes data (see Zaven chart)

## Slide 14: In-Flight Calibration
In-flight calibration verifies ground calibration and accounts for any post-launch shifts in performance
Combination of
  Initial checkout calibration observations
  Joint observations with other X-ray observatories, under cross-calibration working group IACHEC
    Swift XRT, XMM-Newton, Chandra
  Periodic calibration monitoring
Specific notes:
  Absolute time calibration: no absolute in-orbit X-ray timing references at the 100 nsec level
    Clear calibration and characterization of system on ground
  Absolute area calibration: no asolute flux calibrator
    Use cross-calibration with other missions
    Intercalibrate individual modules so NICER produces consistent results with minimal adjustment to ground-based caibration efficiencies

## Slide 15: In-Flight Calibration Plan 1
Purpose | Target(s) | Method
XTI-to-Star Tracker Offset, PSF/Off-axis Performance | Crab | Initial Checkout. Multiple rasters/scans across Crab, X-ray centroid of count rate vs. known J2000 position of Crab. Expect ~arcsec centroid accuracy. Orbit night.
Threshold Scan | Stowed | Scan thresholds with no signal to determine optimal threshold level.
XTI-to-Star Tracker Offset, PSF/Off-axis Performance | Crab, Sco X-1 | Orbit day. Additional scans in different thermal configurations to verify thermal analysis. Maintenance observations every 1 month early on.

## Slide 16: Alignment & Response of 56 Telescopes
Each individual optic tip/tilted w.r.t. observatory axis
For each realization of observatory-target offset, determine optic target offset angle and vignetting
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
Target in Obs. coord (one realization)
Indiv. Optic vignetting in Observatory coord

## Slide 17: In-Flight Calibration Plan 2
Purpose | Target(s) | Method
Gain Scale, Energy Resolution | 1E 0102.2-7219 | Initial Checkout. Observe ~60 ksec; approx. 36000 ct/FPM. Lines < 2 keV
Gain Scale, Energy Resolution | Cas A (20 ksec) Cyg X-3 (10 ksec) Perseus Galaxy (60 ksec) SS 433 (20 ksec; X-CAL) GX 301-2? | Initial Checkout. Approx 100000 ct/FPM. Lines 2-6.4 keV
Contamination | 1E 0102.2-7219 | Periodic Monitoring. Observe 5-10 ksec/month; detect array-level gain shifts and contamination trends

## Slide 18: Low Energy Gain Scale: E0102 Supernova Remnant
IACHEC Continuum/Line Model courtesy E. Miller
60 ksec
per FPM
Gain scale to <1%

## Slide 19: High Energy Gain Scale: Circinus Galaxy
Molendi et al 2014 Model
60 ksec
per FPM
Line Centroids
to 10 eV (<1%)

## Slide 20: In-Flight Calibration Plan 3
Purpose | Target(s) | Method
Broad Band Effective Area | PKS 2155-305 (X-CAL) 3C 273 | Initial Checkout. Observe 30 ksec, simultaneous with XMM-Newton or Chandra. Tie overall flux scale.
Broad Band Effective Area Pulse Timing FPM-to-FPM variation | Crab | Initial Checkout. Observe 10 ksec on-axis, broad band continuum source. Known intrinsic flux variability at ~5-10% level. Pulse folding at 33 msec period. Simultaneous with Swift for timing ~100 usec timing tie.

## Slide 21: In-Flight Calibration Plan 4
Purpose | Target(s) | Method
Background | Blank Sky | Initial Checkout. Observe 100 ksec various blank sky targets. Verify and refine background model. RXTE background points. Chandra Deep Field or Lockman Hole ROSAT ¼ keV background map (hot & cold spots) For sensitive targets, offset points
Background | Blank Sky | Maintenance. Observe 20-60 ksec per month, blank sky targets, intensive after Soyuz configuration change

## Slide 22: In-Flight Calibration Plan 5
Purpose | Target(s) | Method
UV Loading | Beta Car, Beta Leo, Vega | Initial check-out. On-off pointings. Measure detector response to UV loading
Threshold Throughput Efficiency | Crab | Initial check-out. Continuum source at low energies to verify throughtput at threshold edge.
Continuum shape and low energy threshold response | Crab | Maintenance. 5 ksec per month. Continuum response changes.

## Slide 23: In-Flight Background Characterization
Post-launch background calibration observations
  Dedicated blank sky observations
  Data collected during slews between targets
  Dedicated off-pointed background observation before/after faintest targets
  Dark data in stowed configuration will be collected
Verify and refine ground-based background modeling approach
Deep 100 ksec observation of blank sky during initial checkout (~3 calendar days) to characterize background behavior w.r.t. orbit and pointing position w.r.t. Soyuz
  100 ksec @ (0.17 + 0.13) ct/s = 30000 ct (0.4-8 keV)
    Enough counts to detect 10% variations over 25 minute timescale (< 90 minute orbit)
    Also able to fold with orbital period, geomagnetic cut-off rigidity, etc. to build significance
  536 ct/FPM
    Enough counts for crude spectrum, and to detect ~5% FPM-to-FPM variations
    17000 ct 0.4-2 keV; 13000 ct 2-10 keV
Routine maintenance background calibration observations to continuously assess background environment (~monthly 20-60 ksec & off-target background points)
Compare to non-imaging RXTE Proportional Counter Array, able to ultimately achieve background model with 1% r.m.s. unmodeled component (Markwardt was PCA background modeling lead scientist from 2003-2012)

## Slide 24: Response Matrix Calculation
Thermal Film Transmission
Vignetting Cube
ARF (per XRC)
XRC Transmission
Off-axis response
Attitude Data
Co-Alignment
ARF Calculator (versus time)
=
✕
✕
RMF (per XRC)
Window Transmission
FPM RMF
E
E
E
E
Threshold Setting
RMF Calculator
SDD QE & Re-distribution
✕
=
E,q
q
E,PHA
PHA
E,PHA
Sum Over Enabled FPMs

## Slide 25: Calibration Products
All files delivered to the HEASARC Calibration Database (CALDB) for use in standard HEASoft software
Algorithms coded in NICER-specific HEASoft tasks
  Effective Area calculator
  Adjustment of X-ray event times for time calibration
Optics Response Model
Ancillary Response File (Effective Area) & Off-axis Algorithms
Detector Response Model
Response Matrix File (56 FPMs)
Gain Calibration
nicerpi (Gain Correction)
Timing Calibration
nicertimecal (Time Correction)