## Slide 1
Einstein Probe mission &
EP-WXT pathfinder LEIA
Zhixing Ling (NAOC)
Instr. scientist of WXT
PI of LEIA
On behalf of EP consortium
2023 April 15th IACHEC meeting

## Slide 2: Main science objectives
Discover otherwise quiescent black holes at almost all astrophysical mass scales and other compact objects by capturing their transient X-ray flares
Detect and localize the electromagnetic-wave sources of gravitational-wave events by synergy with gravitational-wave detectors
Systematic survey of soft X-ray transients and variability of X-ray sources with unprecedented combination of sensitivity and cadence

## Slide 3: Instruments & spacecraft
Wide-field X-ray Telescope
WXT (12 modules)
Follow-up X-ray Telescope
FXT (2 units)
Optics: lobster-eye MPO
Detectors: CMOS
FoV: 3,600 sq deg (1.1 sr)
Band: 0.5 – 4 keV
Spatial resolution: ~ 5’ (FWHM)
Effective area : 2 - 3 cm2 @1keV
Optics: Wolter-1
Detectors: pn-CCD
FoV: ~1 deg
Band: 0.3 -10keV
spatial resolution: <30” (HPD, on-axis)
Effective area: 300 cm2 @1keV (x 2 units)
Orbit: 600 km
Inclination: < 30°
Life : 3 + 2 years
Weight: 1.3 ton
PI : Prof. Weimin Yuan

## Slide 4: Wide-field X-ray Telescope (WXT)
36 MPO plates
4 BI CMOS
6cm x 6cm each
radiator
One of 12 WXT modules
Focal length: 375mm
eff. area: ~3 cm2 @1keV (PSF centre)
Measured PSF
@ NAOC/CAS
Proposed by Angle 1979
double reflection
single reflection

## Slide 5: X-ray CMOS detector
We customized a large-format CMOS sensor for EP-WXT.
From 2015-2020. More than 100 chips are fabricated.
specification:
Size: 6.1 cm × 6.1 cm
Array: 4096 × 4096 pixels
FWHM: ~200 eV @5.9 keV (140 eV@20℃，after gain correction)
Frame rate: 20Hz （boost to 100 Hz）
Feature:
  Fast readout
  radiation harden (No CTI)
  higher temperature (-30℃ is Ok)
  On-chip analog/digital electronics
  Low cost (1/3 of CCD)
To our knowledge:
                This is first time the CMOS sensor used in X-ray astronomy.
            One of the largest Si image sensor in space. WXT will use 48 sensors (1700 cm2 total).
Wu et al 2022, 2023

## Slide 6: Follow-up X-ray Telescope (FXT)
ESA/MPE
ESA/
MediaLario
Joint developed by IHEP/CAS, ESA and MPE
X-ray optic systems
  ESA + MPE
  eROSITA design
X-ray cameras
  PN-CCD module (MPE)
MM-A
ESA/MPE
MPE
(eROSITA FS)
MM-B
For more details. Please refer to Juan and Chengkui’s talk.

## Slide 7: WXT sensitivity & FoV
LEIA in-orbit observation.
~ 3 x10-11 erg/s/cm2 @1ks
WXT will search the transient onboard in real time and publish the information by internet. FXT will slew to the transient in 3 minutes.
Positioning accuracy : < 2 arcmin mostly, ~ 1 arcmin for bright sources (90% error)
FoV size compared with typical GW source locus
# transients per week
EP: >10
Swift: 2.5
MAXI: 0.8

## Slide 8: Science team and data policy
We have built the STP team recently, total 100 scientists.
China : 75
  ESA : 10
  MPE: 10
  CNES: 5
  The data will only accessible to team members within a proprietary period (6 month/ 1 year).
  For more details, please refer to http://ep.bao.ac.cn.
Executive Committee | 
Erik Kuulkers | ESA
Kirpal Nandra | MPE
Weimin Yuan (Chair) | CAS
Shuang-Nan Zhang | CAS

## Slide 9: Simulation of 1 day survey by WXT
In 3 orbits (~ 5hr) WXT covers once the night sky; cover the whole sky in half a year
Galactic coordinates
1 day sky coverage

## Slide 10
2022.5~11
2022.10~12
CDR
Thermal Test
2023.7
2023.8
2023.10
Launch
2022.3
SC PFM FM Units Ready
2023.4
2023.3~5
2023.6
FM Electrical Interfaces and Functions Test
We are here.
Satellite Assembly and E2E Test
SIRR
（S/C Integration Readiness Review ）
Vibration test
Electro magnetic compatibility（EMC ）test
Magnetic test
Flight acceptance review
（FAR）
2023.11
Launch campaign
Phase D Schedule
2023.5
FXT FM ready
12 WXT FM ready

## Slide 11: WXT pathfinder: Lobster Eye Imager for Astronomy (LEIA)
Pathfinder: one WXT test module aboard CAS’s SATech-01
Proposed in 2019.
600 km SSO orbit.
95 minute period
26 + 27kg, 85 W
1 pointing per orbit
(10 – 15 minutes).
10 orbit per day.
CAS’s SATech-01 credit: MicroSAT
launched 2022 July 27

## Slide 12: LEIA first light: Galactic Centre
Instrument test observations: August 8-10, 2022
FoV 340 deg2
Size of full Moon
~800s exposure

## Slide 13: LMC monitoring
700s observation
1 CMOS image (1/4 FoV of module)

## Slide 14: Image and spectrum
Cygnus loop
Sco X– 1
Cas A (SNR)

## Slide 15: LEIA’s transient: stellar flares and GRBs
LXT 221107A super flare
LXT221107A
LEIA X-ray Lightcurve
NICER
Swift
last about 1 week.
Transient rate: 1 per (1 - 2) weeks.
EP will be 30-40 times of LEIA .
Followed up by :
GRB230307A

## Slide 16: LEIA’s all sky survey
Finished 90% of whole sky over last 5 months

## Slide 17: Summary
Einstein Probe will be a powerful mission. It will be launched in 2023.
    3600 deg2 Fov for WXT(find the transient), 600 cm2 effective area of FXT (follow up automatically)
    Two new technology are used: MPO optics and CMOS sensor.
All of the instrument (2 FXT, 12 WXT) have been finished and will be calibrated recently.
For future, Synergy and follow up with/by other in-orbit/ground facilities offers great science opportunities.
lingzhixing@nao.cas.cn http://ep.bao.ac.cn