## Slide 1: Towards an Absolute Flux Calibration of RXTE PCA
Craig Markwardt
RXTE / PCA Team

## Slide 2: Overview
What is RXTE PCA?
Two absolute geometric area estimates
Application to Crab & Cas A
  Flux offset of 5.6%
Crab as a flux transfer standard

## Slide 3: Rossi X-ray Timing Explorer
Launched December 1995
Terminated January 2012
All-Sky Monitor (ASM)
High-Energy X-ray Timing Experiment (HEXTE)
Proportional Counter Array (PCA)
  5 “identical” collimated Xenon-filled proportional counter units (PCUs)
  2-60 keV

## Slide 4: Proportional Counter Array (PCA)
Each unit is a collimated proportional counter
  5 collimator modules
  3-layer Xenon active volume
  Propane and side Xenon veto layers
COLLIMATOR

## Slide 5: RXTE PCA Layer Highlight
Note: discovered that Xenon diffuses into the propane layer over time
PROPANE VETO
REAR/SIDE VETO
XENON (3-layers)
WINDOWS

## Slide 6: What Started This
A colleague walked into my office with old PCA flight hardware, offered it to me
Collimators & PCU mechanical housing / aperture
Can use to measure geometric area?
  Two estimation methodologies
    “First Principles” from my measurements
    Pre-launch optical throughput measurements
Later information that ground-measured PCA geometric area was not used in flux calibration
  Zombeck spectrum / flux normalization was simply assumed!

## Slide 7: Method 1: ”First Principles” Measure Flight-like Hardware
Need to build a realistic model of geometric area / blockages
PCU Aperture “Shoe”
PCU Collimator Module

## Slide 8: Outer Epoxy and Outer Walls
Measured dimension of two existing flight-like collimator modules
Epoxy filling of outer exposed hexagonal cells
Collimator open fraction due to cell walls

## Slide 9: Reference Mirror
0.5” x 0.5” reference flat used for module alignment

## Slide 10: Shoe Support Structure
Measured dimensions from existing flight-like PCU shoe

## Slide 11: X-ray On-Axis Throughput Loss
In-flight Crab scan measurements
  Collimator model (red)
  Fit using same formula as ground-based optical measurements (green)
  Total decrement 8% due to random misalignment of collimator cells
8%
RXTE PCA Crab Scans
Ideal
Realistic
Off-Axis Angle

## Slide 12: Method 2: Pre-Launch Optical Throughput Measurements
Measurements provided by colleague as a spreadsheet + additional notes
Measure a collimator unit as-built
  Placed on an optical table
  Tip-tilt to achieve max throughput
  With-without collimator to measure total on-axis throughput

## Slide 13: Pre-Launch Throughput Measurements
Optical throughput measurements on tip/tilt stage
  Also no-optic measurement
Measurements yield
  Module alignment
  Total throughput
  Random collimator cell misalignments
PCA CDR (1991)

## Slide 14: Optical Throughput Numbers
A total of 45 collimator module measurements are documented
  Only 25 actually flew
  But we don’t know which modules flew or on which PCUs!
We know that as-built all units had very similar open area and alignment
Use top 66% (32 measurements) as indicator of the flight quality units

## Slide 15: Summary
Accounting of both methodologies
  “First Principles”
  “Optical Throughput”
  Nearly, but not entirely independent
Answer very similar!
Shoe Aperture
Collim Aperture
Collim Walls
Edge Epoxy
On-axis Loss
Collim Aperture
Shoe Aperture
Optical Throughput
“First Principles”
Optical Throughput

## Slide 16: PCU Geometric Area
Two separate measurements
  FP = 1628 ± 11 cm2
  Opt = 1646 ± 9 cm2
Weighted mean
  1638.15 ± 7.1 cm2
First Principles
Optical Throughput

## Slide 17: Problem: Entangled Parameters
I can’t just “use” these geometric area values in response calculator since geometric area was optimized along with other parameters in 2012
Geometric area is correlated / entangled with other important parameters
  Xenon density
  Propane density
  Xenon leakage rate
  Detector escape model
Necessitates re-fitting response from scratch
Use newly (re)discovered knowledge!
Fitting process for Crab data
  Remember there are 5 PCU detectors x 3 layers = 15 spectra per observation!
  Include 2.2 – 3 keV as a bonus!
  Used 20 Crab observations spaced over time
  Crab model: tbabs*pow (index free, norm varies with time)

## Slide 18: Fit Residuals: 20 Observations
PCU 0
PCU 1
PCU 2
PCU 3
PCU 4
Layer 1
Layer 2
Layer 3
Energy (2-60 keV)

## Slide 19: Comparing Old versus New Response
Old parameters highly correlated, unphysical
New fitted parameters comply with expected geometric area and Xenon densities
Previous results (Shaposhnikov et al 2012) appear to have been numerically trapped in shallow minimum in chi-square space
Old Parameters
Geometric Area
Total Xenon Density
New Parameters
A Priori Expectation

## Slide 20: Crab Fit Results
Flux smaller by 5.6%
Comparison to Weisskopf et al 2010
  Measurements from 1974-1992
  New result more consistent with historical
Power law index 2.111
  Compare 2.106 (Madsen et al 2017)
Weisskopf et al 2010

## Slide 21: Cassiopeia A Results
Cas A: very different spectrum compared to Crab (Therm + PL ind ~3)
Flux offset 6%, no spectral shape changes, as desired
New Model New Response
New Model Old Response
6%

## Slide 22: Crab as a Flux Transfer Standard
We now know that Crab is not constant (Wilson-Hodge et al 2010), BUT
Use absolute flux measurements (PCA & NuSTAR) to anchor flux scale
Fermi GBM, Swift BAT, and RXTE ASM long-term light curves to extend flux scale over ~27 years
Tie to other observatories
Need to consider that Crab pulsar flux decreases ~0.2% per year due to spindown
Still needs work!
PCA
NuSTAR
Wilson-Hodge et al 2010

## Slide 23: Summary
New RXTE PCA absolute effective area calibration to ~1%
Fluxes are 5.6% smaller compared to previous release in 2012
No apparent spectral shape differences
Planned release this Summer