## Slide 1
The energy calibration of eROSITA
Konrad Dennerl, MPE
IACHEC, 2023 April 25
Pelham, Germany

## Slide 2
Energy Calibration: some eROSITA Specialties
onboard:
  use of precomputed threshold maps for optimizing telemetry
  compression mode ‚PMENV2‘ for scientific data
  compression mode ‚PMALLSINGLES‘ for 55Fe data
ground processing:
  utilization of subpixel resolution
  fast PSF focal plane mapping at high count rates
  use of constant energy thresholds (in eV)
  improved noise suppression for >1 pixel patterns
  floating point PI values
  RMFs and ARFs with non-constant bin sizes
  CTI and gain adjustments to varying CCD temperatures
  automatic refinement of RMFs and ARFs
efficiency:
  only ~5 days needed for initial energy calibration on ground
  only ~2 days per year needed for energy calibration in space

## Slide 3
Energy Calibration: some eROSITA Specialties
onboard:
  use of precomputed threshold maps for optimizing telemetry
  compression mode ‚PMENV2‘ for scientific data
  compression mode ‚PMALLSINGLES‘ for 55Fe data
ground processing:
  utilization of subpixel resolution
  fast PSF focal plane mapping at high count rates
  use of constant energy thresholds (in eV)
  improved noise suppression for >1 pixel patterns
  floating point PI values
  RMFs and ARFs with non-constant bin sizes
  CTI and gain adjustments to varying CCD temperatures
  automatic refinement of RMFs and ARFs
efficiency:
  only ~5 days needed for initial energy calibration on ground
  only ~2 days per year needed for energy calibration in space

## Slide 4
eROSITA Specialties

## Slide 5
Energy Calibration: some eROSITA Specialties
onboard:
  use of precomputed threshold maps for optimizing telemetry
  compression mode ‚PMENV2‘ for scientific data
  compression mode ‚PMALLSINGLES‘ for 55Fe data
ground processing:
  utilization of subpixel resolution
  fast PSF focal plane mapping at high count rates
  use of constant energy thresholds (in eV)
  improved noise suppression for >1 pixel patterns
  floating point PI values
  RMFs and ARFs with non-constant bin sizes
  CTI and gain adjustments to varying CCD temperatures
  automatic refinement of RMFs and ARFs
efficiency:
  only ~5 days needed for initial energy calibration on ground
  only ~2 days per year needed for energy calibration in space

## Slide 6
without subpixel resolution
with subpixel resolution
from IACHEC 2011
eROSITA Specialties
utilizing subpixel resolution for the mirror calibration

## Slide 7
eROSITA Specialties
fast PSF Focal Plane Mapping at high count rates

## Slide 8
Energy Calibration: some eROSITA Specialties
onboard:
  use of precomputed threshold maps for optimizing telemetry
  compression mode ‚PMENV2‘ for scientific data
  compression mode ‚PMALLSINGLES‘ for 55Fe data
ground processing:
  utilization of subpixel resolution
  fast PSF focal plane mapping at high count rates
  use of constant energy thresholds (in eV)
  improved noise suppression for >1 pixel patterns
  floating point PI values
  RMFs and ARFs with non-constant bin sizes
  CTI and gain adjustments to varying CCD temperatures
  automatic refinement of RMFs and ARFs
efficiency:
  only ~5 days needed for initial energy calibration on ground
  only ~2 days per year needed for energy calibration in space

## Slide 9
released charge cloud in eV
released charge cloud in adu
  pattern recognition with constant energy thresholds in eV
the charge cloud..
..as it is created
..as it appears (gain & CTI)
split thresholds for TM4 in adu, computed for 65 eV
TM4, Fe-K
eROSITA Specialties

## Slide 10
Energy Calibration: some eROSITA Specialties
onboard:
  use of precomputed threshold maps for optimizing telemetry
  compression mode ‚PMENV2‘ for scientific data
  compression mode ‚PMALLSINGLES‘ for 55Fe data
ground processing:
  utilization of subpixel resolution
  fast PSF focal plane mapping at high count rates
  use of constant energy thresholds (in eV)
  improved noise suppression for >1 pixel patterns
  floating point PI values
  RMFs and ARFs with non-constant bin sizes
  CTI and gain adjustments to varying CCD temperatures
  automatic refinement of RMFs and ARFs
efficiency:
  only ~5 days needed for initial energy calibration on ground
  only ~2 days per year needed for energy calibration in space

## Slide 11
original patterns
rejected patterns
accepted patterns
-
=
-
=
150 eV (!)
novel method for suppressing low energy detector noise
eROSITA Specialties

## Slide 12
Energy Calibration: some eROSITA Specialties
onboard:
  use of precomputed threshold maps for optimizing telemetry
  compression mode ‚PMENV2‘ for scientific data
  compression mode ‚PMALLSINGLES‘ for 55Fe data
ground processing:
  utilization of subpixel resolution
  fast PSF focal plane mapping at high count rates
  use of constant energy thresholds (in eV)
  improved noise suppression for >1 pixel patterns
  floating point PI values
  RMFs and ARFs with non-constant bin sizes
  CTI and gain adjustments to varying CCD temperatures
  automatic refinement of RMFs and ARFs
efficiency:
  only ~5 days needed for initial energy calibration on ground
  only ~2 days per year needed for energy calibration in space

## Slide 13
  usage of ARFs and RMFs with non-constant bin sizes to avoid overhead in storage and to increase the performance in spectral fits
https://wiki.mpe.mpg.de/eRosita/erocalib_calibration
  computation of floating point PI values to avoid unneccessary binning artefacts
physical energy axis:
< 8 keV: small bins near lines and absorption edges
≥ 8 keV: large bins at high energies
instrumental energy channel axis:
< 8 keV: bin size matches energy resolution
≥ 8 keV: large bins
eROSITA Specialties
  floating point PI values, binning of ARFs and RMFs

## Slide 14
Energy Calibration: some eROSITA Specialties
onboard:
  use of precomputed threshold maps for optimizing telemetry
  compression mode ‚PMENV2‘ for scientific data
  compression mode ‚PMALLSINGLES‘ for 55Fe data
ground processing:
  utilization of subpixel resolution
  fast PSF focal plane mapping at high count rates
  use of constant energy thresholds (in eV)
  improved noise suppression for >1 pixel patterns
  floating point PI values
  RMFs and ARFs with non-constant bin sizes
  CTI and gain adjustments to varying CCD temperatures
  automatic refinement of RMFs and ARFs
efficiency:
  only ~5 days needed for initial energy calibration on ground
  only ~2 days per year needed for energy calibration in space

## Slide 15
Energy Calibration: some eROSITA Specialties
onboard:
  use of precomputed threshold maps for optimizing telemetry
  compression mode ‚PMENV2‘ for scientific data
  compression mode ‚PMALLSINGLES‘ for 55Fe data
ground processing:
  utilization of subpixel resolution
  fast PSF focal plane mapping at high count rates
  use of constant energy thresholds (in eV)
  improved noise suppression for >1 pixel patterns
  floating point PI values
  RMFs and ARFs with non-constant bin sizes
  CTI and gain adjustments to varying CCD temperatures
  automatic refinement of RMFs and ARFs
efficiency:
  only ~5 days needed for initial energy calibration on ground
  only ~2 days per year needed for energy calibration in space

## Slide 16
TM7 (FM1): Jan 18-22
TM2 (FM2): Feb 17-26
TM1 (FM3): Mar 15-22
TM4 (FM4): Apr 07-14
TM5 (FM5): Apr 25-28
TM3 (FM7): Jun 09-13
TM6 (FM6): Jun 27-30
Energy ground calibration in 2016
mainly long flatfield exposures
energies: C-K, O-K, Cu-L, Al-K, Ti-K, Cu-K, Ge-K
CCD temperature: -95°C
event rate: ~2100 events/s
TM7
TM2
TM1
TM4 TM5
TM3 TM6

## Slide 17
eROSITA Energy Calibration:
Ground

## Slide 18
example: Fe-K, measured with FM4
Reconstructing the spectral distribution requires
pattern recognition
correction for gain variations between CCD channels
correction for charge transfer loss (CTI)
gain determination

## Slide 19
CTI determination
 CTI = 2.1×10-5
emission line determined in 130 (adaptively computed) macro pixels containing a minimum of 30 first singles around the line
CCD column 240 (arbitrary choice)
CTI = 2.1 x 10-5
Reconstructing the spectral distribution requires
pattern recognition
correction for gain variations between CCD channels
correction for charge transfer loss (CTI)

## Slide 20
CTI determination

## Slide 21
plot contains 47 267 data points
each data point is the result of several iterative template fits
example: Fe-K, measured with FM4
CTI determination

## Slide 22
8 calibration energies
CTI determination

## Slide 23
8 energies
7 CCDs
all 7 CCDs calibrated with 3.3 billion events

## Slide 24
individually for each CCD column
CTI
gain
Energy interpolation of the CTI and gain

## Slide 25
reconstructed spectral distribution
example: Fe-K, measured with FM4
Reconstructing the spectral distribution requires
pattern recognition
correction for gain variations between CCD channels
correction for charge transfer loss (CTI)
FWHM = 132.5 – 143.1 eV, all photons: FWHM = 137.8 eV
accuracy of absolute energy scale: ± 2 eV (± 0.03%)
raw data
singles
doubles
triples
quadruples
all valid patterns

## Slide 26
Energy resolution obtained for
single pixel events in comparison
with theoretical limit (dashed curve)
energy [keV]
energy [keV]
energy [keV]
FWHM [eV]
FWHM [eV]
FWHM [eV]
Spectrum of Boron and Carbon emission lines
FWHM ~ 49 eV

## Slide 27
Baikonur, Kazakhstan, 2019 July 13

## Slide 28
Energy calibration with the internal 55Fe source
Mn-K
Al-K Ti-K

## Slide 29
Energy Calibration: internal calibration source

## Slide 30
Gain: TM 4, Al-K
ground calibration

## Slide 31
Gain: TM 4, Al-K
in-orbit calibration

## Slide 32
CTI: TM 4, Al-K
ground calibration

## Slide 33
CTI: TM 4, Al-K
in-orbit calibration

## Slide 34
eROSITA Energy Calibration:
Space

## Slide 35
two unexpected effects
Energy calibration in space
Light leak in TM5 and TM7
CCD temperatures 10°-15°C higher

## Slide 36
two unexpected effects
one expected effect
Energy calibration in space
CTI increase due to radiation damage
also „gain“ decrease due to CTI increase in the framestore region
Light leak in TM5 and TM7
CCD temperatures 10°-15°C higher

## Slide 37
two unexpected effects
one expected effect
Energy calibration in space
CTI increase due to radiation damage
also „gain“ decrease due to CTI increase in the framestore region
and one ‚missing‘ effect
no signs for any contamination (!)
Light leak in TM5 and TM7
CCD temperatures 10°-15°C higher

## Slide 38
two unexpected effects
one expected effect
Energy calibration in space
CTI increase due to radiation damage
also „gain“ decrease due to CTI increase in the framestore region
and one ‚missing‘ effect
no signs for any contamination (!)
Light leak in TM5 and TM7
CCD temperatures 10°-15°C higher

## Slide 39
Challenges for the energy calibration:
1) CCD temperatures (Sep 2019 – Feb 2022)
ground calibration at -95°C
first 55Fe measurements after launch

## Slide 40
CCD temperatures during the first 55Fe measurements after launch
(major) challenge:
develop a temperature
model for gain and CTI

## Slide 41
1
2
3
4
5
ground calibration at -95°C
Challenges for the energy calibration:
2) CTI increase due to radiation damage

## Slide 42
Challenges for the energy calibration:
2) CTI increase due to radiation damage

## Slide 43
CCD column specific CTI evolution
TM1, Al-K
Feb 2022
Aug 2021
Feb 2021
Nov 2020
Nov/Dec 2019
1

## Slide 44
CCD column specific CTI evolution
TM1, Al-K
Feb 2022
Aug 2021
Feb 2021
Nov 2020
Nov/Dec 2019
2

## Slide 45
CCD column specific CTI evolution
TM1, Al-K
Feb 2022
Aug 2021
Feb 2021
Nov 2020
Nov/Dec 2019
3

## Slide 46
CCD column specific CTI evolution
TM1, Al-K
Feb 2022
Aug 2021
Feb 2021
Nov 2020
Nov/Dec 2019
4

## Slide 47
CCD column specific CTI evolution
TM1, Al-K
Feb 2022
Aug 2021
Feb 2021
Nov 2020
Nov/Dec 2019
5

## Slide 48
eROSITA CCD
CTI increase in frame store area appears as gain [adu/eV] decrease

## Slide 49
CCD column specific ‚gain‘ evolution
TM1, Al-K
TM1, Ti-K
TM1, Mn-K
peak position [adu]
CCD column number
CCD column number
CCD column number

## Slide 50
2021
2020
2023
2022
2025
2024
Expected CTI increase @ 5.9 keV
eROSITA
XMM / EPIC-pn

## Slide 51
Energy calibration: results 1) 55Fe calibration data

## Slide 52
Testing the energy calibration
1) internal calibration source
1
2
3
4
5
ground calibration at -95°C

## Slide 53
TM1
Nov 2020
Feb 2021
Aug 2021
Feb 2022
TM1
TM1
TM1
TM2
TM2
TM2
TM2
TM3
TM3
TM3
TM3
TM4
TM4
TM4
TM4
TM6
TM6
TM6
TM6
2
3
4
5

## Slide 54
TM1
Nov 2020
Feb 2021
Aug 2021
Feb 2022
TM1
TM1
TM1
TM2
TM2
TM2
TM2
TM3
TM3
TM3
TM3
TM4
TM4
TM4
TM4
TM6
TM6
TM6
TM6
2
3
4
5
Al-K: absolute energy scale accurate to ± 1 eV (despite CCD temperature changes and CTI increase)

## Slide 55
Energy calibration: CTI and spectral resolution
TM1
TM2
TM3
TM4
TM6
CTI
FWHM (singles)
1.5 keV
4.5 keV
5.9 keV

## Slide 56
Energy calibration: results 2) diffuse X-ray sky

## Slide 57
input: eROdays 43850 .. 48550, in steps of 100 eROdays (except 44850), for TM12346
covering the whole survey period (so far): Dec 2019 – Feb 2022 (with 16.7 day sampling)
Testing the energy calibration
2) diffuse X-ray sky

## Slide 58
Testing the energy calibration
2) diffuse X-ray sky
TM12346 @ eRASS:5
(sampled in steps of 100 eROdays)
O VII: He-like triplet:
560.9 - 568.5 - 574.0 eV
CCD temperature: -86 .. -79 C
threshold: „PMENV2“
E = 568 eV, FHWM = 66.8 ± 0.8 eV
O VII

## Slide 59
TM2 (FM2)
TM3 (FM7)
TM6 (FM6)
TM4 (FM4)
TM1 (FM3)
( TM12346, all valid patterns )
FWHM = 64.0 ± 0.1 eV
ground calibration (2016)
CCD temperature: -95.8 .. -94.2 C
threshold: 46 adu, E = 527 eV
eRASS:5 (2019-2022)
CCD temperature: -65 .. -79 C
threshold: „PMENV2“, E = 568 eV
FWHM = 66.8 ± 0.8 eV
diffuse X-ray sky (2019-2022)
Comparison with ground calibration

## Slide 60
TM2 (FM2)
TM3 (FM7)
TM6 (FM6)
TM4 (FM4)
TM1 (FM3)
( TM12346, all valid patterns )
FWHM = 64.0 ± 0.1 eV
ground calibration (2016)
CCD temperature: -95.8 .. -94.2 C
threshold: 46 adu, E = 527 eV
eRASS:5 (2019-2022)
CCD temperature: -65 .. -79 C
threshold: „PMENV2“, E = 568 eV
FWHM = 66.8 ± 0.8 eV
diffuse X-ray sky (2019-2022)
Comparison with ground calibration
Similar energy resolution (O VII) in space as on ground (O-K), despite:
O VII emission intrinsically broadened
  561.0 eV (f)
  568.7 eV (i)
  574.0 eV (r)
mean energy higher than 537 eV (O-K)
CCD temperature 10-15°C higher and variable
CTI increase

## Slide 61
Energy calibration: results 3) RXJ1856 and 1E0102

## Slide 62
requirements:
‚correct‘ physical model
‚correct‘ RMFs and ARFs
Testing the energy calibration
3) RXJ1856 and 1E0102

## Slide 63
General properties of the ARF and RMF
spectral model
RMF
ARF
observed pulse height distribution
known
known
ARF: „Ancillary Response File“, RMF: „Redistribution Matrix File“

## Slide 64
General properties of the ARF and RMF
spectral model
RMF
ARF
observed pulse height distribution
known
known
ARF: „Ancillary Response File“, RMF: „Redistribution Matrix File“

## Slide 65
General properties of the ARF and RMF
spectral model
RMF
ARF
known
known
observed pulse height distribution
typically several million elements
 HUGE parameter space!
typically ~1000 elements (comparatively trivial)
ARF: „Ancillary Response File“, RMF: „Redistribution Matrix File“

## Slide 66
ARF: „Ancillary Response File“, RMF: „Redistribution Matrix File“
General properties of the ARF and RMF
RMF
ARF
spectral model of 1E0102
spectral model of RXJ1856
observed spectrum of RXJ1856
observed spectrum of 1E0102
RX J1856-3754
1E 0102.2-7219
normalization
gain
normalization
ARF: 4 free parameters
RMF: 25 free parameters

## Slide 67
χν2 = 1.1
offset = -1 eV
TM 3
1E 0102.2-7219
RX J1856-3754
„Fitting“ the RMF and ARF
Method:
consider two sources with „reliable“ spectral models simultaneously:
RX J1856-3754
& 1E 0102.2-7219
χν2 = 0.9
TM 3
χν2 = 2.2
offset = +1 eV
TM 3
χν2 = 1.5
TM 3

## Slide 68
V. Burwitz
RXJ 1856
Chandra LETG
nH = (7.2 +/- 0.3) × 1019 cm-2, kT = 62.4 +/- 0.4 eV, norm = (1.58 +/- 0.06) x 105 [tbabs * bbodyrad]
RX J1856-3754: Chandra LETG
Χ2 = 694, ndof = 1251

## Slide 69
only 1 free parameter:
normalization
(4 central pixels ignored)
nH = 7.25 × 1019 cm-2
kT = 62.4 eV
(Chandra LETG)
χν2 = 1.8
χν2 = 2.4
χν2 = 1.7
χν2 = 2.1
χν2 = 1.9
TM 1
TM 2
TM 3
TM 4
TM 6
„before“
RX J1856-3754
2020 Apr 01-02
all valid patterns

## Slide 70
χν2 = 1.2
χν2 = 1.1
χν2 = 1.1
χν2 = 1.3
χν2 = 1.3
RX J1856-3754
2020 Apr 01-02
all valid patterns
only 1 free parameter:
normalization
(4 central pixels ignored)
nH = 7.25 × 1019 cm-2
kT = 62.4 eV
(Chandra LETG)
TM 1
TM 2
TM 3
TM 4
TM 6
„after“

## Slide 71
RX J1856-3754
2020 Apr 01-02
single pixel events
only 1 free parameter:
normalization
(4 central pixels ignored)
nH = 7.25 × 1019 cm-2
kT = 62.4 eV
(Chandra LETG)
χν2 = 1.1
χν2 = 1.0
χν2 = 1.1
χν2 = 0.9
χν2 = 1.1
TM 1
TM 2
TM 3
TM 4
TM 6
„after“

## Slide 72
1E 0102.2-7219: IACHEC !

## Slide 73
eROSITA calibration observations of 1E 0102.2-7219
1
2
3
2019 Nov 07-08
2020 Jun 18-19
2021 Nov 26-27
8 C
Chandra ACIS
3 long (30-60 ks)
pointed eROSITA observations
2019 - 2021

## Slide 74
χν2 = 1.7
χν2 = 1.4
χν2 = 1.9
χν2 = 1.4
χν2 = 1.0
1E 0102.2-7219
2019 Nov 07-08
all valid patterns
offset = -2 eV
offset = -3 eV
offset = -2 eV
offset = -2 eV
offset = +2 eV
TM 1
TM 2
TM 3
TM 4
TM 6
1
original IACHEC model used
  only 2 free parameters:
offset and normalization

## Slide 75
χν2 = 1.2
χν2 = 1.1
χν2 = 1.6
χν2 = 1.6
χν2 = 1.3
1E 0102.2-7219
2020 Jun 18-19
all valid patterns
offset = -3 eV
offset = -5 eV
offset = +3 eV
offset = -3 eV
offset = -1 eV
TM 1
TM 2
TM 3
TM 4
TM 6
2
original IACHEC model used
  only 2 free parameters:
offset and normalization

## Slide 76
χν2 = 1.7
χν2 = 1.7
χν2 = 1.1
χν2 = 1.4
χν2 = 1.5
1E 0102.2-7219
2021 Nov 26-27
all valid patterns
original IACHEC model used
  only 2 free parameters:
offset and normalization
offset = -4 eV
offset = +1 eV
offset = +2 eV
offset = -2 eV
offset = +2 eV
TM 1
TM 2
TM 3
TM 4
TM 6
3

## Slide 77
χν2 = 1.7
χν2 = 1.2
χν2 = 1.2
χν2 = 1.1
χν2 = 0.9
1E 0102.2-7219
2020 Jun 18-19
single pixel events
offset = -3 eV
offset = -2 eV
offset = -1 eV
offset = -3 eV
offset = +4 eV
TM 1
TM 2
TM 3
TM 4
TM 6
1
original IACHEC model used
  only 2 free parameters:
offset and normalization

## Slide 78
χν2 = 1.1
χν2 = 1.2
χν2 = 1.1
χν2 = 1.2
χν2 = 1.0
1E 0102.2-7219
2020 Jun 18-19
single pixel events
offset = -3 eV
offset = -1 eV
offset = +2 eV
offset = -3 eV
offset = -1 eV
TM 1
TM 2
TM 3
TM 4
TM 6
2
original IACHEC model used
  only 2 free parameters:
offset and normalization

## Slide 79
χν2 = 1.2
χν2 = 1.2
χν2 = 1.0
χν2 = 1.2
χν2 = 1.2
1E 0102.2-7219
2021 Nov 26-27
single pixel events
offset = -1 eV
offset = +4 eV
offset = +1 eV
offset = -1 eV
offset = +1 eV
TM 1
TM 2
TM 3
TM 4
TM 6
3
original IACHEC model used
  only 2 free parameters:
offset and normalization
1E0102 is an ideal source for benchmark tests of the energy calibration accuracy
the eROSITA results are consistent with the IACHEC model
despite (sometimes very large) changes
in the CCD temperature, the absolute energy scale can be reconstructed to an
accuracy of ≈ 3 eV
independent of the pattern size
over a time span of 2 years

## Slide 80
The energy calibration of eROSITA
Konrad Dennerl, MPE
IACHEC, 2023 April 25
Pelham, Germany