## Slide 1: Overview of EP-FXT
Yong Chen
On behalf of FXT team of IHEP
May 13, 2024
16th IACHEC meeting Parador de Granjia
20240513-16

## Slide 2: Outline
FXT on-orbit commission
FXT performance
Summary

## Slide 3: FXT configuration
: European Space Agency
: Max Planck Institute for Extraterrestrial Physics
: Innovative Academy for Microsatellites, CAS
: Institute of High Energy Physics, CAS
: Technical Institute of Physics and Chemistry, CAS
*All other unmarked contributions of FXT are provided by IHEP
ESA
MPE
ESA
ESA
MPE
MPE
pnCCD
IHEP
IAMC
TIPC
ESA
MPE
IAMC
IHEP
TIPC
IAMC
MA A | MA B
FM2 of ESA | eROSITA FS of MPE
Electron diverter A | Electron diverter B
ED FM2 of ESA | ED FM of CAS
electron diverter

## Slide 4: FXT on-orbit commission
January 10: Sunshade cover A/B was unlocked;
January 11-24: FXT baking process;
January 25-26: pnCCD-A was powered on; background and mode testing;
February 5: pnCCD A/B were powered on and worked normally;
February 22: Cover of FXT-A opened, observing M87;
February 28: Cover of FXT-B opened, and both FXT units observed Crab simultaneously;
March 5: pnCCD-A radiation source test;
April 5: pnCCD-B radiation source test.

## Slide 5: FXT thermal control
-Y
+Y
The FXT thermal control subsystem is working normally in orbit
The temperature and temperature control stability of each component in the early stage of orbit, baking stage, and normal observation stage all meet the corresponding requirements
The power consumption of the FXT thermal control subsystem is normal
Mirror
Shielding box
Detector container
Filter wheel

## Slide 6: Refrigerator and detector temperature
Chart: 时间/min
Chart: 时间/min
The temperature stability meets the technical specifications: the temperature control target point of pnCCD-A is -95 ℃; pnCCD-B is -90.95 ℃, with fluctuations of ± 0.05 ℃ during long-term continuous operation.
Stable output power of refrigeration unit: Refrigerator A has an output power of 16.5 ± 1W; Refrigerator B has an output power of 18.5 ± 1W，both with a significant cooling margin.

## Slide 7: Electronics units functionality & performance
Both detector-boxes have undergone work mode testing and have completed
FXT-A: Full Frame, Partial-window, Timing and Power saving mode
FXT-B: Full Frame, Partial-window, Timing mode
Command reception and execution are normal
Scientific and engineering data are normal
The pnCCD detector is operating normally and its performance meets expectations
The two detector boxes are operating normally
Partial-window mode image
Timing mode processed image

## Slide 8: Filter wheel
6 operating positions/filters:
Open
Thin filter（80 nm Al+200 nm PI）
Medium filter（200 nm Al+400 nm PI)
Hole filter（hole; 80 nm Al+200 nm PI）
Closed（2mm-thick Al）
Calibration（Fe-55）
Medium filter
Thin filter
Hole filter
Closed
Open
Calibration

## Slide 9: FXT commission
March 5-19:
NGC 2516: Coordinate Conversion Matrix
Crab: Time System
Omega Centauri: Coordinate Conversion Matrix
3C 273 and SRGA J144459.2-604207: Angular resolution; optimize the mirror temperature.
Vela X and M87: Imaging quality, E-C calibration, effective area calibration.
The performance meets the requirements, and detailed calibration analysis is needed in the future.

## Slide 10: On-orbit Fe-55 measurement
Al-K
Si-K
Cl-K
Ca-K
Escape peak
Mn-Kα
Mn-Kβ
Energy Resolution：
98 eV@1.5 keV
162 eV@5.9 keV

## Slide 11: PSF measurements (phase 1)
3C273

## Slide 12: In-orbit particle background
eROSITA particle background
FXT particle background
The count rate of particles background of FXT is about 1/5 of that of eROSITA
Variation of particle background count rate with orbital position
Count rate
Longitude
Latitude

## Slide 13: FXT observation of M87 and Crab
Feb. 22, FXT-A observation of M87
Feb. 28，FXT-A&B observation of Crab
FXT-A
FXT-A
FXT-B

## Slide 14: M87
M87
FXT A&B；0.3-10 keV
Thin filter; FoV 1°x1°
Exposure time: 39 ks
Suzaku
XIS FoV
XMM-Newton MOS FoV
Chandra ACIS-I
FoV
M87 FXT-A
Overlaid with LOFA contour
Cold front
SDSS optical image

## Slide 15
M87 spectrum
model：tbabs*（vmekal1+vmekal2）
FXT spectrum

## Slide 16: Crab observation
FXT-A Partial Window mode
Medium filter; Exposure time: 2.6ks
0.3-10 keV
Pulse profile
FXT-B Timing mode
Exposure time: 2.6 ks
0.3-10 keV
P=33.823961 ms
1 arcmin

## Slide 17
FXT observation of PSR B1821-24
Exposure time：32 ks
period：3.054 ms
FXT mode：timing mode

## Slide 18: Puppis A (SNR)
Puppis A
FXT A&B; 0.3-10 keV
Thin filter; FoV: 1°x1°
Exposure time: 9ks
FXT-A spectrum
O VIII
Ne IX
Ne X
Mg XI
Si XIII
S XV
Ar XVII
O VII
Fe XVII

## Slide 19
Puppis A SNR:
images of the distributions of the elements O VIII, Ne IX, and Mg XI
O VIII
RGB
Mg XI
Ne IX

## Slide 20: Omega Centauri
Omega Centauri
Exposure time: 68 ks
FXT A&B; 0.3-10 keV
Thin filter; FoV: 1°x1°
20 arcmin
Image size: 20 x 20 arcmin

## Slide 21
FXT-A
FXT-B
Medium filter, Full Frame mode, exposure ~40000 s, 0.3-10 keV
139 sources detected by FXT-A，with 38 cataloged sources (1eRASS，4XMM，2RXS，2SXPS）
134 sources by FXT-B，with 44 cataloged sources
~100 new sources detected!
3C273
FXT observation of the sky region around 3C273

## Slide 22: Follow-up observation of transient EP240420a
FXT conducted the follow-up observation about 2 hours after the WXT detection.
Flux: 1.2e-12 erg/s/cm2
About 9” away from the optical counter part
FXT-B; Medium filter; FoV: 1°x1°
Exposure time: 9.5 ks
0.3-10 keV

## Slide 23: 3. Summary
The FXT instrument is operating normally in orbit
FXT has good in-orbit performance and meets the requirements
The particle induced background is very low for FXT
Preliminary science results have been obtained
Detailed calibration will be conducted in the next step
Thanks!

## Slide 24: Partial-window mode and timing mode parameter optimization
Partial-window mode and timing mode are newly developed modes compared to eROSITA
The parameters were optimized in-orbit
The optimized discharge time is set to 200 microseconds
Operate stably for observations
Crab
PW mode
Crab
timing mode

## Slide 25: FXT thermal control: early in orbit
Mirror
Early in orbit:
The temperature of each component meets the storage temperature requirements.
The actual measurement of thermal control is consistent with expectations and meets the requirements.
Refrigerator
compressor
Unfolding mechanism &
locking mechanism

## Slide 26: FXT thermal control: baking stage
Baking stage:
The temperature of each component meets the storage temperature requirements
Unfolding mechanism &
locking mechanism
Mirror
Detector container

## Slide 27: Test & calibration status
 | Test item | Requirements | Test results
1 | FXT power on | Normal | normal
2 | Unlock, unfold the sunshade cover | Normal | All successful
3 | Refrigerator temperature control | PNCCD temperature control to target temperature ± 0.5 ℃ (-95 ℃ ≤ target temperature ≤ -85 ℃) | Temperature stability ≤ 0.5 ℃
4 | Detector working mode | Full frame, Partial-window and Timing mode | Working modes are all normal
5 |  | Three working states: normal, offset calibration, and SAA | Working states are all normal
6 | X-ray imaging | Energy range：0.5 keV~8 keV | 0.3 keV~10 keV
7 |  | Effective area：≥100 cm2@1.25 keV，on axis | Roughly consistent with ground test; ~300 cm2@1.25 keV (Further detailed calibration needed)
8 |  | Angular resolution：≤2′ HPD | A：23.7’’ ; B： 20.1’’; on axis, 20℃
 | item | requirement | Test result
 | Source location accuracy | < 20″(90% C.L.)，J2000 | < 10” (90% C.L.) J2000 (still optimizing)
Notes: 有效面积，标定文档上看现在得到的值fxta到是差不多，fxtb的似乎比文档上的还好。根据李承奎M87的弥散arf和点源arf的比例，得到修正后的fxta 中膜的arf~286cm^2@1.25keV。