## Slide 1: Large Segmented Optics Paper proposal
Kristin K. Madsen
Goddard Space Flight Center

## Slide 2: Large segmented optics
1.7m
(Not selected)
AXIS, NASA probe
Lynx, NASA Flagship concept
3 m
(Earliest selection 2030)
2.4 m
(launch 2039)
NewAthena, ESA flagship

## Slide 3: Assembly and Calibration
Mirror Module
Optical axis
Focal length

## Slide 4: Horizontal beamline: XRCF
Simulated X-Ray Beam
X-ray beam 1.47m diameter
Sized for Chandra
Athena X-ray optic 2.4m diameter
Each of the six mirror sectors would be tested individually, with the results combined (‘stitched’) to obtain the full mirror performance

## Slide 5: Vertical beamline: VERT-X

## Slide 6: System optical axis
OA vector
Mirror node
X-ray
RF
x
*
x
*
Mirror Assembly Axis
OA

## Slide 7: Mirror Node and Optical axis: XRCF
The determination of the optical axis is the most challenging measurement.
mirror node location with respect to the MCS
tilt of the OA with respect the MCS.
MCS = Mirror Coordinate System is defined by metrology
Mirror
OAsystem
Misaligned MM
Mirror node location by 150 µm
Determine OA direction by 10”
Must use vignetting curves to determine the OAsys direction

## Slide 8: Calibration Requirements
Each mirror module needs OA and Focal length measured to XX and YY
  Needed for installation to obtain target PSF
The system must measure OA and Focal length to XX and YY
  Requires the re-measurement of each mirror module as installed in the mirror assembly to KK and ZZ with respect to a mirror coordinate system
Parameter | Functionality & Core Test | FM calibration
Xray Optical axis | ≤20'' with 68% confidence | ≤30'', with 99.7% confidence
Focal length | ≤ 1mm with 99.7% confidence | ≤1 mm, with 99.7%
Example requirements:

## Slide 9: Demands on facilities
Number of mirror modules can be in the hundreds!
Mirror modules are generally small
  Can be done at multiple and smaller beamlines
  Could mount multiple mirror modules in chamber/beamline at same time
Still, it will take at least a day to characterize each module
  Example: NewAthena (15 rows) has 600 mirror modules, which would take >2 years assuming 250 workdays a year
Then after integration the system OA and focal length must be determined
  Requires a large specialized calibration facility
  High in cost

## Slide 10: To what degree can simulations replace actual measurements?
Can we device accurate enough metrology to skip steps?
To what degree do we need to X-ray characterize individual mirror modules?
Can we rely on X-ray measurements from individual mirror modules together with metrology to predict the integrated system performance?

## Slide 11: Paper Proposal
Have the WG produce a paper that discusses:
  The challenges with segmented optics calibration
  Makes predictions
  Makes recommendations
Helps NewAthena
Helps future proposals for large segmented optics