## Slide 1
NICER Calibration Status Craig Markwardt (NASA/GSFC) on behalf of NICER Team (esp. Jeremy Hare & Keith Gendreau)
GSFC
IACHEC April 2026

## Slide 2: NICER’s Unique Capabilities
Launched June 2017 to International Space Station
Spectral band: 0.2–12 keV (52 silicon detectors)
Energy resolution: < 150 eV @ 6 keV
Timing resolution: 100 nsec RMS absolute
Non-imaging field of view (“single-pixel”)
  6 arcmin diam. (half-max)
High throughput (3.5 Crabs with no pileup)

## Slide 3: NICER Calibration Status
NICER Crab
NICER calibration very stable
Major impact of optical light leak & repair
  Expected gain shifts
  Expected ARF adjustments
Other calibration aspects
  Energy scale: monitoring drifts of few eV / yr
  ARF: systematic feature errors <1.5% (0.4-10 keV)
  RMF: Scholze & Procop X-ray silicon model performs well

## Slide 4: Outline
NICER Mission Status
NICER Calibration Status
Optical Light Leak, Repair and Mitigation
  NICER repair spacewalk successfully patched the largest optical leaks
  Additional optimizations significantly improve NICER performance during orbit day
Future Calibration Plans

## Slide 5: NICER Mission Status
As of June, 2025, NICER has suspended scientific operations
NICER operations is focused on maintaining a safe environment aboard the International Space Station for crew and robotic vehicles
NICER continues to fund US observers through its GO program, at least for the coming year
NICER science operations will focus on providing the best science calibration and archival data access

## Slide 6: Loss of Pointing Control
In June, 2025, NICER’s azimuth drive no longer fully responded to pointing commands
  This axis is driven by harmonic drive gearing
No longer possible to track astrophysical targets
NICER detectors were operated in a fixed-pointing mode for about two weeks
  Gather additional sky and particle background data
  Science operations were suspended in August, 2025
Team is working on a procedure to place NICER in a “safe” stowed position
Example of Harmonic Drive
Wikipedia

## Slide 7: NICER Science Calibration and Pipeline Efforts
Although NICER science operations are suspended, the NICER team will continue to improve the science calibration using existing data sets
The NICER team will improve the science data processing software
Final archival processing of mission science data with best software and calibration
This effort will take place over the next ~year
Other closeout activities related to supporting grant-holders may extend into following years

## Slide 8: NICER Big Events
May 2023 – Optical Light Leak
Jan 2025 – Optical Light Leak Repair Mission
  Partially successful, but additional damage discovered
Feb-Mar 2025 – Additional MPU configuration changes
  Worked extremely well
June 2025 – Azimuth drive failure

## Slide 9: Light Leak Impacts for Scientists
Increased optical light loading: much higher telemetry loads and data losses
  NICER team improved automatic screening
Extreme loading pushed energy scale out of calibration
  NICER team improved energy scale calibration at high loading
Reduced ToO and long-term monitoring opportunities
  NICER avoided targets within ~100 deg of sun during orbit day
  Lower level X-ray threshold increased to ~0.43 keV during orbit day to avoid noisy telemetry
  NICER team implemented MPU configuration changes to reduce deadtime, streamline on-board event production, and telemeter more accurate information
X-ray performance changed as expected because of repair patches
  Data during orbit night was still excellent, much of orbit day data is excellent as well, within observing constraints
  No detectable change to X-ray throughput for modules because of known holes, to within few percent (Jeremy Hare work)
  X-ray throughput changed because of crew-installed patches
    NICER team validated changes (Jeremy Hare work)

## Slide 10: Nick Hague and Repair Kit on ISS

## Slide 12: High Resolution Digital Imagery Reveals Details
Over 400 digital pictures taken by Nick Hague showed many details including many small pin holes as well as possible stress on the thermal films

## Slide 13: Additional Read-Out Optimizations
The NICER team did a deep scrub of the MPU parameters, and developed optimized settings
  Tested & verified in the laboratory February 2025
  Table upload in March 2025
These new optimizations do not reduce optical loading, but do
  Reduce telemetry rate
  Reduce onboard MPU processing deadtime
  Improve accuracy of onboard housekeeping for use in science analysis software
  Greatly enhance recovery of good science data
Allowed productive NICER observations during orbit day over a much larger field of regard (sun angle > 80 deg instead of >110 deg)

## Slide 14: Post-Repair Calibration Work
Revised ARF to science community
  Overall ~2% change due to patch blockages
  Validation observations of Crab agree with expectations within a few percent
Improved screening for observers
  Separate criteria for orbit day and night
  Improved automatic screening that attempts to keep the good data amongst the bad, rather than excluding any data with bad quality

## Slide 15: Further Calibration Updates (~Year)
Several known minor problems in response generation
  Expect ~5% change in flux scale
    Based on improved deadtime understanding
  Expect 0.05 change in power law shape
    Remove non-physical fit of optic geometric area
  Expect low energy threshold shift ~5 eV
    Based on observations of HZ43, RX J1856, Crab

## Slide 16: Swift Observatory Update
Swift spacecraft predicted for re-entry in ~August this year!
NASA approved a reboost operation
  LINK rendezvous spacecraft provided by Katalyst
  Launch June – last Pegasus vehicle
  Rendezvous ~4 weeks later, reboost operation taking few weeks
Swift instruments have been idled or powered down since Feb/March in order to conserve power
Significant commissioning effort required after reboost complete and instruments powered on