## Slide 1
Pelham/Germany 18th IACHEC meeting, 20-23 April 2026 K. Dennerl / MPE
Behind the scenes of eROSITA:
how we transmit the data
Notes: 20 min

## Slide 2
~170 million photons in 6 months  ~11 photons per second  easy to transmit
Why is the transmission of X-ray CCD data challenging ?

## Slide 3
~170 million photons in 6 months  ~11 photons per second  easy to transmit
X-ray CCDs and the
low energy threshold

## Slide 4
The absorption of an X-ray photon generates a charge cloud which may extend over several pixels.
In order to reconstruct the energy of the incoming photon, it is necessary to collect all the charge components.
X-ray CCDs and the low energy threshold

## Slide 5
The absorption of an X-ray photon generates a charge cloud which may extend over several pixels.
In order to reconstruct the energy of the incoming photon, it is necessary to collect all the charge components.
This, however, is limited by the presence of noise, which is steeply rising towards the lowest energies.
It becomes necessary to introduce a low energy threshold and to ignore the charges below.
X-ray CCDs and the low energy threshold
charge [adu,≈eV]
event rate
eROSITA CCD

## Slide 6
The low energy threshold may influence the pixel pattern which we see
very low threshold
low energy threshold
low threshold
high threshold
very high threshold
quadruple
triple
double
single
X-ray CCDs and the low energy threshold

## Slide 7
The low energy threshold may influence the pixel pattern which we see
very low threshold
low threshold
high threshold
very high threshold
quadruple
triple
double
single
X-ray CCDs and the low energy threshold
 the observed pixel pattern depends on the low energy threshold

## Slide 8
very low threshold
low threshold
high threshold
very high threshold
X-ray CCDs and the low energy threshold
 the spectral resolution depends on the low energy threshold
low energy threshold: ≈ 40 eV
TRoPIC spectrum of C-K (0.28 keV), derived from single pixel events
low energy threshold: ≈ 100 eV

## Slide 9
X-ray CCDs and the low energy threshold
doubles: spatial resolution in one dimension
singles: no spatial resolution
triples: spatial resolution in two dimensions
quadruples: spatial resolution in two dimensions
illustration for a low energy threshold of 1%
the spatial resolution is better than the pixel size

## Slide 10
doubles
singles
triples
quadruples
0.5%
1%
2%
3%
4%
doubles
singles
triples
quadruples
only one parameter: low energy threshold [%]
X-ray CCDs and the low energy threshold
 the spatial resolution depends on the low energy threshold

## Slide 11
Comparison of X-ray CCD images without and with subpixel resolution

## Slide 12
Comparison of X-ray CCD images without and with subpixel resolution

## Slide 13
X-ray CCDs and the low energy threshold
The problem with a spatially constant low energy threshold:
ground calibration of TM6: all events with PHA above 67 adu
noise is not uniformly distributed over the CCD
a subset of pixels may occupy a major fraction of telemetry
the low energy threshold has to be set to an unnecessarily high value for the majority of the pixels
charge [adu,≈eV]
event rate

## Slide 14
X-ray CCDs and the low energy threshold
Motivation for applying adaptive thresholds:
charge [adu,≈eV]
event rate
By slightly reducing the low energy thresholds in noisier regions, a lot of telemetry can be saved.
The saved telemetry can be utilized for reducing the thresholds in larger area.
better spectral and spatial resolution (though not homogeneous over the CCD)
determination of pixel specific thresholds so that each (unexposed) pixel uses about the same telemetry

## Slide 15
We can transmit ~ 5 events/frame per CCD  ~ 0.68 events/ks per pixel
an average pixel may produce ‚signal‘ above the event threshold only once every ~25 min
exposure times of ~hours are required to find suitable thresholds
computation not possible in space
upload not feasible after launch
thresholds need to be determined before launch and uploaded into onboard memory
Noise may be higher in space by an unknown amount
possibility to scale uploaded threshold maps by a commandable factor
computation of threshold maps: for each individual pixel determine the minimum adu value above which a rate of ~0.68 events/ks results
Determination of adaptive „threshold maps“

## Slide 16
Determination of adaptive „threshold maps“
take long ‚dark‘ measurements on ground
determine for each pixel the event rate as a function of the low energy threshold
find a value which yields an event rate of ~0.68 events/ks
insert this value into a ‚threshold map‘
side remark: MIPs rate: ~2 MIPs per frame, each MIP affecting n pixels
 event rate: n x 4 x 104 / ks
 regions affected by MIPs have to be excluded from telemetry;
the effect of area removal can be approximated by deadtime

## Slide 17
acceptable event rate
X-ray CCDs and the low energy threshold
total event rate of one specific pixel (290,117) as a function of the low energy threshold:
28.3 min ‘dark’ exposure in ground calibration
corresponding threshold
5.0 efc

## Slide 18
acceptable event rate
X-ray CCDs and the low energy threshold
total event rate of one specific pixel (290,345) as a function of the low energy threshold:
28.3 min ‘dark’ exposure in ground calibration
corresponding threshold
5.0 efc

## Slide 19
TM5 ‘noise‘ map (measures the event rate variability)
TM5 threshold map
X-ray CCDs and the low energy threshold
5.0 efc
5.0 efc
5.0 efc
5.0 efc

## Slide 20
threshold maps determined on ground for 5 events/frame/camera, and uploaded to the onboard memory before launch
TM 7
TM 6
TM 5
TM 4
TM 3
TM 2
TM 1
X-ray CCDs and the low energy threshold

## Slide 21
Situation before launch:
concept of adaptive threshold maps promising.
BUT: would we be able to downlink an event rate of ~ 5 events/frame/camera just for the noise plus the real X-ray photons ?
5 events/frame/camera would need about 2 hours of antenna time per day, exceeding the guaranteed time.
Risk that the performance of the instrument cannot be fully utilized due to telemetry limitations.

## Slide 22
What can be transmitted per day without compression
guaranteed downlink rate for eROSITA: 176.9 MB/hour

## Slide 24
Save telemetry by transmitting only the „important“ regions, i.e. the regions around charges which are likely to have been released by X-ray photons
concept of „event islands“ (also applied in other X-ray missions)
concept of two low energy thresholds:
a trigger threshold for locating a major charge
a split threshold for locating secondary ( = minor = supplementary ) charges around a major charge
good to know: in the case of eROSITA, the maximum observable pattern size which can be created by an X-ray photon is 2 x 2 pixels
Event compression: general concept

## Slide 28
Two threshold approach:
primary (`trigger‘) threshold: applied to all pixels
secondary (`split‘) threshold: applied only around `trigger‘ pixels
45
4
„ENVTAB“ = 9
13
13
„ENVTAB“ = 0
Data compression: transmission of whole 8 pixel environment does not require more bits than transmission of triggering pixel
Restriction: available adu range restricted, 10 combinations supported
Energy thresholds applied in the onboard processing mode ‚PMENV2‘
20
9
„ENVTAB“ = 4
18
10
„ENVTAB“ = 3

## Slide 29
18
10
direct neighbour
diagonal neighbour
dynamic range: 18  0 .. 17
0: charge 1 adu below threshold or primary pixel
1: charge 2 adu below threshold
15: charge 16 adu below thr.
16: charge at least 17 adu below thr.
17: charge unknown (edge, bad, MIP)
dynamic range: 10  0 .. 9
0: charge 1 adu below threshold or primary pixel
1: charge 2 adu below threshold
7: charge 8 adu below thr.
8: charge at least 9 adu below thr.
9: charge unknown (edge, bad, MIP)
Example: event compression for the „10|18“ case

## Slide 30
Example: event compression for the „10|18“ case
18
10
direct neighbour
diagonal neighbour
dynamic range: 18  0 .. 17
0: charge 1 adu below threshold or primary pixel
1: charge 2 adu below threshold
15: charge 16 adu below thr.
16: charge at least 17 adu below thr.
17: charge unknown (edge, bad, MIP)
dynamic range: 10  0 .. 9
0: charge 1 adu below threshold or primary pixel
1: charge 2 adu below threshold
7: charge 8 adu below thr.
8: charge at least 9 adu below thr.
9: charge unknown (edge, bad, MIP)

## Slide 31
values in one CCD frame [adu] (after offset and common mode subtraction)
Example: event compression for the „18|10“ case

## Slide 32
values in the threshold map [adu]
Example: event compression for the „18|10“ case

## Slide 33
insensitive pixel (edge, bad, MIP)
trigger pixel (charge at or above threshold)
Example: event compression for the „18|10“ case

## Slide 34
Example: event compression for the „18|10“ case

## Slide 35
no other pixel in the environment contains charge within the available dynamic range
 no environment transmitted
pixel (008_007_00070) is a triggering pixel which will be transmitted anyway
Example: event compression for the „18|10“ case
 lack of transmitted environment contains information (and does not cost any telemetry!)
telemetry stream:
|008_008_00090|

## Slide 36
Example: event compression for the „18|10“ case
telemetry stream:
|008_008_00090|
|005_007_00067|08_16_08_16_00_08_16_01|
pixel (006_007_00088) is not considered in the decision whether the environment should be transmitted, because it is a triggering pixel which will be transmitted anyway
but pixel (006_006_00048) contains charge
within the available dynamic range
 environment transmitted

## Slide 37
telemetry stream:
|008_008_00090|
|005_007_00067|08_16_08_16_00_08_16_01|
|006_007_00088|08_10_08_00_16_08_01_08|
Example: event compression for the „18|10“ case
pixel (005_007_00067) is not considered in the decision whether the environment should be transmitted, because it is a triggering pixel which has already been
transmitted
but 2 pixels contains charge
within the available dynamic range
 environment transmitted

## Slide 38
Example: event compression for the „18|10“ case
telemetry stream:
|008_008_00090|
|005_007_00067|08_16_08_16_00_08_16_01|
|006_007_00088|08_10_08_00_16_08_01_08|
|008_007_00070|08_00_08_16_16_08_05_08|
pixel (008_008_00090) is not considered in the decision whether the environment should be transmitted, because it is a triggering pixel which has already been
transmitted
but pixel (008_006_00044) contains charge
within the available dynamic range
 environment transmitted

## Slide 39
Example: event compression for the „18|10“ case
telemetry stream:
|008_008_00090|
|005_007_00067|08_16_08_16_00_08_16_01|
|006_007_00088|08_10_08_00_16_08_01_08|
|008_007_00070|08_00_08_16_16_08_05_08|
|004_005_00055|09_16_08_17_16_09_11_08|
|007_003_00054|08_16_09_16_17_03_16_09|
|002_002_00059|
Result:
17|09: pixel in insensitive area (additional diagnostic information)
16|08: upper adu limit (value outside dynamic range)
0..15|0..7: adu value in telemetry

## Slide 40
transmitted environment values
same telemetry as that required for the uncompressed transmission of 12 pixels, but information about 46 pixels
number of pixels with
adu ignored due to MIPs: 6
rough upper limits: 11
sensitive upper limits: 17
known adu values: 12
---
46
number of 32-bit words: 12
Example: event compression for the „18|10“ case
telemetry stream:
|008_008_00090|
|005_007_00067|08_16_08_16_00_08_16_01|
|006_007_00088|08_10_08_00_16_08_01_08|
|008_007_00070|08_00_08_16_16_08_05_08|
|004_005_00055|09_16_08_17_16_09_11_08|
|007_003_00054|08_16_09_16_17_03_16_09|
|002_002_00059|

## Slide 41
reconstructed adu values
Example: event compression for the „18|10“ case
x
insensitive area
trigger pixel, charge known
neighbour pixel, charge known
‘critical’ pixel, charge ≥ 40 adu may be present
uncritical upper limit, ’clean’ pixel
uncritical diagonal neighbour pixel
result from pattern recognition for a constant threshold for of 41 adu
(everything below 41 adu is ignored)

## Slide 42
invalid because next to insensitve area
invalid because of shape
invalid because no triggering pixel (only present in telemetry because next to triggering pixel)
charge cannot be reconstructed,
potentially invalid shape
 only two valid photon events recognizable
reconstructed adu values
Example: event compression for the „18|10“ case
result from pattern recognition for a constant threshold for of 41 adu
(everything below 41 adu is ignored)

## Slide 43
Testing the event compression algorithm
Data taken in parallel in uncompressed and compressed mode (in April 2018).
After decoding the compressed data, all 3.2 million events agreed exactly in position and charge.

## Slide 44
threshold maps determined on ground for 5 events/frame/camera, and uploaded to the onboard memory before launch
TM 7
TM 6
TM 5
TM 4
TM 3
TM 2
TM 1
X-ray CCDs and the low energy threshold
on ground

## Slide 45
TM 7
TM 6
TM 5
TM 4
TM 3
TM 2
TM 1
X-ray CCDs and the low energy threshold
x 1.18
x 1.14
== 125 adu
x 1.14
x 1.16
x 1.20
== 145 adu
scaling factors applied since eROday 43421
constant thresholds used for TM 5 and TM 7
in space

## Slide 46
spatially constant threshold
spatially variable threshold
X-ray CCDs and the low energy threshold
result of the spatially variable threshold applied to in-flight data:
in space

## Slide 47
45
4
Dynamic range setting after launch
18
10

## Slide 48
TM6 primary thresholds:
5 ecf threshold map, multiplied with 1.14
45
4
„ENVTAB“ = 9
TM6 secondary thresholds for main directions:
ENVTAB = 9: primary thresholds – 44 adu
Energy thresholds applied in the onboard processing mode ‚PMENV2‘
adu
adu

## Slide 49
TM6 primary thresholds:
5 ecf threshold map, multiplied with 1.14
TM6 secondary thresholds for main directions:
ENVTAB = 9: primary thresholds – 44 adu
Energy thresholds applied in the onboard processing mode ‚PMENV2‘
adu
adu
primary threshold: ~73 adu
secondary threshold: ~30 adu

## Slide 50
Data processing on ground:
general idea: remove spatial threshold inhomogeneities
before ‘eSASS_947‘ processing: constant threshold of 46 adu applied
consistent processing of TM12346 data possible for almost all threshold settings, however:
for many data, split threshold cut unnecessarily high
constant adu threshold does not mean constant eV threshold (gain, CTI)
( spectral and spatial resolution still position dependent)
improvement in ‚eSASS_947‘: apply threshold which is constant in eV

## Slide 51
TM7: 125 eV
TM6: 50 eV
TM5: 105 eV
TM2: 60 eV
TM1: 50 eV
TM4: 55 eV
TM3: 60 eV
Threshold maps
(in adu) used in „947“ and „948“ processing
(this is not the lower end of the eROSITA bandpass - it is the lower limit to which secondary charges can be collected)

## Slide 52
threshold map consequences: TM2, all valid patterns, eROdays 48144 – 48199
0.5 – 2.5 keV
6% less flux in 947 & 948 compared to 946
946
947 948
947 948
946
worst case
224 hours (9.3 days) exposure

## Slide 53
TM7: 125 eV
TM6: 50 eV
TM5: 105 eV
TM2: 60 eV
TM1: 50 eV
TM4: 55 eV
TM3: 60 eV
Threshold maps
(in adu) used in „947“ and „948“ processing

## Slide 54
TM7: 125 eV
TM6: 60 eV
TM5: 105 eV
TM2: 70 eV
TM1: 60 eV
TM4: 65 eV
TM3: 70 eV
Threshold maps
(in adu) used after „948“ processing

## Slide 55
ç√
ç√
Consequences of threshold map choice
60 eV 46 adu
70 eV 46 adu
TM2 0.4 - 0.6 keV
94.9 % of ‘46 adu’ photons
100.0 % of ‘46 adu’ photons

## Slide 56
effect can be exactly quantified
correction straightforward, but requires reprocessing
in the ‚947‘ and ‚948‘ processing, the thresholds had been choosen by ≈10 eV too low
noise events made otherwise valid pixel patterns invalid
≤ 6% flux loss and spatial inhomogeneities (but higher spectral resolution)
eROSITA event compression
the onboard event compression algorithm PMENV2 works so efficiently that the performance of eROSITA is not limited by telemetry (!)

## Slide 57
Behind the scenes of eROSITA:
how we transmit the data
Pelham/Germany 18th IACHEC meeting, 20-23 April 2026 K. Dennerl / MPE